## Slide 1: Side Scan Survey Acquisition and Processing

## Slide 2: Objectives of this session
Side Scan Theory
Basics of sonar imagery, range, etc.
Surveying Principles
Towed vs. hull-mounted side scan sonars
Surveying speed
Sonar range vs. resolution
Running a Survey
Adjusting your side scan imagery
Marking targets
3
Post Processing
Adjusting your image
Marking targets
Creating mosaics
File Work
Saving post-processed files
Mosaicking batch files
1
2
4
5
6
Configuring Devices
Connecting a side scan device
Configuring as towed or mounted
Notes: Stressed Water Supply
Issue
Maintain the health of traditional water sources and execute a water source diversification strategy
Solution
Xylem’s leading-edge technologies monitor, pump and treat water from all sources and enable water reuse
Aging Infrastructure
Issue
Utilities have to effectively assess and identify high-risk areas for repair/replacement before problems occur
Solution
Xylem’s intelligent pipeline and critical infrastructure services perform condition assessment, identify defective assets, provide bypass services and replacement technologies, reduce or eliminate combined sewer overflows and leaks/non-revenue water
Stormwater & Flooding
Issue
Significant increase in severe weather patterns is causing flooding and related damages to communities
Solution
Xylem’s flood management solutions include sensors for early warnings, dewatering for disaster response, communications for recovery and submersible pumping for resilient infrastructure
Regulatory Compliance
Issue
Utilities must successfully comply with a growing body of compliance regulations
Solution
Xylem’s analytics and sensors evaluate a broad range of water quality parameters, and our technologies treat water and wastewater to meet regulatory standards
Non-Revenue Water
Issue
Utilities have an important opportunity to reduce persistent and costly water losses from leaks and faulty meter readings
Solution
Xylem’s broad portfolio of solutions monitors for, and identifies, water leaks, as well as faulty meters. Our communications network enables point-to-multipoint communications throughout the system
Operating Strategy Reducing Costs
Issue
Utilities want to lower operating and energy costs, and leverage new revenue opportunities
Solution
Xylem offers industry-leading pumping and treatment solutions for energy efficiency, and software-enabled solutions to optimize operations and identify revenue opportunities

## Slide 3: Side Scan Theory

## Slide 4: Side Scan Survey Overview
Uses:
Object detection
  Obstructions
  Search and recovery
  Historical sites
Visual analysis
  Pipelines
  Underwater structures
Geological identification
Notes: More subjective, less objective
Imagery

## Slide 5: What Is Found In A Side Scan Record?
Features on the seafloor create shadows
Water column: sonar (fish) height
Target: some feature or object (generally produce a shadow)
Bottom sediment: will affect return
Water Column
Shadow
Notes: Fish is along center
Like dragging a paintbrush

## Slide 6: The Importance Of The Shadow
Lower towfish, longer shadow
Farther
Closer

## Slide 7: The Importance of the Shadow
The shadow can be more helpful than the shape

## Slide 8: The Shadow Effect
Often the shadow is more recognizable than the object.

## Slide 9: What You Find With A Side Scan Record
T0 (Ping)
T1 (First return)
T2 (range)
T2
Signal Strength vs. Time
T0
T1
T2
T2
T1
Received signal
Time
Time

## Slide 10: What You Find With A Side Scan Record
Signal vs. Time
T1
T1
T0
T2
T2
T0
T1
T2
T2
T1
Time
Time

## Slide 11: Sonar System Components
Sonar->Topside->HYPACK
Topside

## Slide 12: What Is A Side Scan’s Resolution?
Across track resolution
Sonar frequency
Along track resolution
Sonar aperture
  Typically (0.25° to 0.8°).

## Slide 13: Along Track Resolution
Improves closer to sonar
Farther from sonar, objects can merge
Along Track Resolution
Horizontal beam width
Bad 
Good 

## Slide 14: Across Track Resolution
Improves farther from sonar
Nearer to sonar, objects can merge
Across Track Resolution
Bad 
Good 

## Slide 15: Frequency Determines Effective Range
Low frequency:
Long range
Blurrier image
High frequency:
Short range
Sharper image

## Slide 16: Goldilocks Zone
Balances along and across track resolution
  Along track: good up close
  Across track: good far away

## Slide 17: Nadir Gap
Blind spot directly below sonar

## Slide 18: Survey Planning: 100% And 200% Coverage
Signal width:
200m
Line spacing
160 meters
Line spacing
80 meters
Notice the nadir is NOT covered
Nadir is covered here

## Slide 19: Survey Speed
Speed < Max Speed
Speed > Max Speed
Too fast creates gaps

## Slide 20: Side Scan Operations
 | Benefits | Problems
Towed | Close to bottom Minimal motion Deep water | Position imprecise
Hull Mounted | Accurate position Won’t hit bottom Shallow water | Poor for deep water Vessel motion affects data
Towed vs. hull-mounted (fixed) systems

## Slide 21: Towed vs Hull-mounted Side Scan
A side scan “towfish”
A hull-mounted side scan
HYPACK

## Slide 22: Towed Positioning
Boat position is known
Fish position can only be guessed
  USBL can help
?

## Slide 23: Hull-Mounted Offsets
For a hull mount, align your side scan with the vessel keel

## Slide 24: Side Scan Imagery Examples

## Slide 25: Interpreting Color Palettes

## Slide 26: Targets May Be Hard To Identify
This is what a fighter jet looks like when it hits the water very fast.
This is a verified
F-16 after it hit the water.

## Slide 27: Can You Identify This Object?
Hint
The object is upside down.
Pay attention to the shadow.

## Slide 28: Ships On The Seafloor
1
2
Two ships—sunk at different times—at the same location.

## Slide 29: Common Side Scan Issues

## Slide 30: Effect Of Turns On Imagery

## Slide 31: Heave Artifacts

## Slide 32: Roll Artifacts

## Slide 33: Yaw Artifacts

## Slide 34: Generator Noise

## Slide 35: Echosounder Noise

## Slide 36: Electronic Noise

## Slide 37: Good Side Scan Data

## Slide 38: Bad Side Scan Data

## Slide 39: Can You Guess What Happened Here?
The sonar hit the bottom

## Slide 40: The Importance Of Shadows
Shadow beyond end of record = sonar is below the object

## Slide 41: Connecting A Side Scan Device

## Slide 42: Setting Up A Towed Side Scan
Launch Hardware
Right-click “Hardware”, select “Add Mobile”
Select “Hardware” on the left
Under “Side Scan Survey”, check “Include” and “Installed on Towfish”

## Slide 43: Setting Up A Towed Side Scan, Positioning
Select “Boat”, add your positioning device
Select “Mobile”, add “Towfish”
With “Towfish” selected, click “Setup”
1
2
3
4

## Slide 44: Setting Up A Towed Side Scan, Towfish Setup Pt. 1
Important settings:
  Cable counter at top
  Layback method PDF
  A-Frame Offsets
    Measurements from GPS to tow point
  Fish Depth
    Choose sensor to use
    “Shallow Fish” will not use depth

## Slide 45: Setting Up A Towed Side Scan, Towfish Setup Pt. 2
Connection setup:
Select the “Survey Connect” tab
Click “…” button beside “Device Connection”
Configure the connection here
1
2
3

## Slide 46: Setting Up A Side Scan, Device Connection
Select “Side Scan Survey” along left
Select device, click “Add”
Click “Setup” to configure device
Select “Connect” to configure connection
    Some devices must have manufacturer software running
1
2
2
3
4

## Slide 47: Setting Up A Side Scan, Connection Test
Comport Test: Displays comport activity
Network Test:
  Lets you “ping” an address
  Lets you view UDP data
    TCP connections won’t show data here

## Slide 48: Setting Up A Side Scan, Offsets
Position offsets: Relative to vessel (boat or towfish)
    Usually 0 for a towed side scan

## Slide 49: Analog Side Scan
Select NI USB-6221
  Other device is deprecated

## Slide 50: Analog Side Scan: USB-6221
USB connection
Connections:
    AI0 = Port signal
    AI1 = Starboard signal
    AI2 = Trigger
Must install National Instruments software

## Slide 51: Analog Side Scan Software Setup
Launch Side Scan Survey
Use Analog Monitor window to configure side scan
This window must remain open

## Slide 52: Side Scan Operation

## Slide 53: Survey Planning: 100% Coverage
100% coverage:
  Efficient coverage for large areas
  Space lines at twice sonar range
  Subtract some to allow for errors
  E.g. sonar with 100m range, lines spaced ~160m
    100m range x 2 – 40m error = 160m
Signal width:
200m
Line spacing
160 meters

## Slide 54: Survey Planning: 200% Coverage
200% coverage:
  Better imagery coverage
  Bottom is covered twice
  Nadir is covered
  Half line spacings of 100% coverage
Line spacing
80 meters
Signal width:
200m

## Slide 55: Collection: Side Scans Vs. Echosounders
4-5 kts
Do not stop while towing
No turns during collection
Nadir area is obscured
Image courtesy of Jim Kidd

## Slide 56: Side Scan Positioning
Cable out (layback)
Acoustic positioning system (USBL)
ROV
Ship mounted
A-frame for towing a fish behind the vessel

## Slide 57: How To Do An Object Detection Self-check
Run past a known object (buoy, sand waves, etc.)
If you don’t see a known object, you won’t find an unknown object.

## Slide 58: Towfish Height Above The Bottom
Fish height = 8-20% of sonar range
Why?
Provides ideal angle for reflections
Shadows are noticeable but not too long/short
Poor reflections, short shadows

## Slide 59: Running A Survey

## Slide 60: Starting A Survey
Click “Smart Launch Survey”
Side Scan Survey and HYPACK Survey will launch

## Slide 61: HYPACK Survey vs Side Scan Survey?
Both programs run simultaneously
Side Scan Survey:
  Side scan sonar
  Optionally: MRU, heading, pressure sensor
HYPACK Survey:
  Everything else (GPS, single beam, tide data)
HYPACK
SURVEY
SIDE SCAN
SURVEY
GPS
Side Scan Sonar
Your computer

## Slide 62: Window For Display And Control
Alarms:
  Green = Good 
  Yellow = Caution – Bad sensor data
  Red = Danger – No sensor data
System Measurements:
  Boat or towfish

## Slide 63: Waterfall and Signal Graph
Waterfall: Imagery from sonar
Signal graph: Amplitude (signal strength) over time

## Slide 64: Options And Menus
Logging commands sync between Side Scan and HYPACK Survey
Saved as HSX files in Project’s Raw folder
Logging Option:
  File Overlap: New files will overlap with old files for X seconds
  XTF logging: Not recommended. Use HSX Converter afterwards

## Slide 65: Side Scan Device Controls
Tools -> Side Scan Device Control (or Ctrl+Alt+S)
Alternatively, use manufacturer’s software
Warning: | Be careful when making changes here. Adjustments made in the Device Control window DO affect the recorded data.

## Slide 66: Side Scan Buttons
Select display frequency
Select display device
Quick gain settings
Speed compensation
Set bottom track altitude
Capture image
Measure height
Show signal graph
Options
Notes: A_tgt1.avi?

## Slide 67: Real Time Mosaic In HYPACK SURVEY
See real-time mosaics in HYPACK Survey
Chart->Sidescan Mosaic->Enable
  Update: sets when the mosaic will draw

## Slide 68: Adjusting The Image

## Slide 69: First Steps
Click “Sidescan Signal” button
Turn OFF “Processed Signal”
Adjust with buttons on left until signal is roughly halfway
Notes: Processed signal = gains – already looking at output
  unchecked = raw signal – now we see the input
  What gets written to disk

## Slide 70: Signal Window Pt. 2
“Processed Signal” shows gains
“Reset” will automatically set the bars

## Slide 71: Side Scan Controls - Colors
View->Side Scan Controls (or Side Scan Controls button)
All settings apply immediately
Choose and adjust your colors

## Slide 72: Side Scan Controls - Gain
Basic Gains: Not recommended
Auto TVG: “Smart” TVG
  Higher sensitivity = brighter image
  Across-Track Smoothing smooths gain
dBs / 100 Meters: dB multiplier
Formula: Applies shown formula
  ‘r’ is range

## Slide 73: Which Ones Are Best?
Auto TVG
  Fast, simple
dBs / 100 Meters
  More control
  Less artifacts

## Slide 74: Side Scan Controls - Display
Display Optimal Fish Altitude: Marks a red line at 10% of the signal range
Remove Water Column: Leave this unchecked
  Important to see water column while surveying

## Slide 75: Why You Don’t Remove The Water Column
Harder to see your altitude.
If you see something like this…
Speed up or pull the cable in, fast!

## Slide 76: Side Scan Controls – Bottom Tracking
Use HYSCAN Bottom Tracking
  Auto bottom detect
  Uses side scan imagery
  Sensitivity: Higher = lock on to bottom sooner in water column
  Blanking: Ignore this much range
  Gate Size: Look this far up or down from the last ping’s bottom
Use Fish Sensor

## Slide 77: Side Scan Survey Windows

## Slide 78: Side Scan Survey Windows
Sidescan Waterfall: New waterfall window
  Useful for multi-frequency sonars
Tow Fish Altitude
  Configurable window displaying current altitude
Towfish Sensors
  Miscellaneous towfish info

## Slide 79: Side Scan Survey Windows
Coverage map
Graphical HPR

## Slide 80: Side Scan Data Display Windows
Device Selections:
Can select device for certain measurements
Only affects acquisition display

## Slide 81: Marking Targets

## Slide 82: Targeting
Double-click to mark target
Dropdown at top selects recent targets
Click “Retarget” then click in window to move target
Zoom Box and zoom Extents
Image Settings to adjust the image

## Slide 83: Targets Options
Naming style
“Capture adjacent” adjusts number of pings to capture
“Automatic 30%” trims width to 30% of range
JPEG Options:
  Either show water column or slant range correct
  Option to show range ruler

## Slide 84: Image Capture Target
Select the Camera Icon
Click-and-drag to capture image
Image will appear in HYPACK Shell

## Slide 85: Height Measurement
Capture and Measuring a Target
Select the Height Measurement tool
Click on the object you wish to measure

## Slide 86: Height Measurement
Fish altitude: Drag to bottom
Range to object: Drag to object
Object Height: Drag to end of shadow

## Slide 87: Processing

## Slide 88: Data Flow
Mosaic Data Flow
HYSWEEP SURVEY
SIDE SCAN
SURVEY
SIDE SCAN MOSAIC PROGRAM
(HYSCAN)
HSX
HSX
Side Scan Data
TIF
24 or 8 bit
TIF
TIF
TIF
Line 1
Line 2
Line 3
TGT
Mosaics
TIF
TIF
TIF
Targets
Average Backscatter Data from Multibeam
Entire Data Set
Individual tifs can be created from each line, or a single tif from all lines
Targets can be saved into a report and displayed in Target Viewer.
HSX files created in Data Converter
HS2 or XTF
3rd PARTY SIDE SCAN
FILES
CM2
JSF
SDF
XTF
Notes: 88

## Slide 89: Menu Icons
Icons in Side Scan Mosaic
Load Files (HSX, HS2, XTF, JSF, SDF, CM2)
Save to HS2 File
Raw Data Mode – displays altitude, heading, and tracks
Scan View – displays waterfall and target captures
Mosaic View – dialog for creating mosaic
Redraw Screen
Sidescan Controls
Next/Previous Line Selection
Remove Line
Notes: 89

## Slide 90: Processing Stage 1: Raw View
Side Scan Mosaic Processes
Load files – HSX, HS2, XTF, JSF, SDF, or CM2 files
Adjust:
  Bottom track
  Smooth heading
  Smooth track line
Notes: 90

## Slide 91: Processing Stage 2: Scan View
Side Scan Mosaic Processes
Scan View
Adjust color, gain, TVG, and display options
Create targets and images
Notes: 91

## Slide 92: Processing Stage 3: Mosaic
Side Scan Mosaic Processes
Create georeferenced mosaics
Notes: 92

## Slide 93: Loading and Stage 1

## Slide 94: Loading a File, pt. 1
Select “Open File”
Open either the Raw or the Edit folder
  Raw: Survey files
  Edit: Modified files
Select the lines you are interested in

## Slide 95: Loading a File, pt. 2 (Read Parameters)
Selections: Choose devices
Device Info: Set offsets
Survey Info: Basic data from the survey
Advanced:
  Smooth bottom track, heading, or navigation
  Adjust bottom track up/down
Notes: Attempt to match devices between files: For example, if, in file 1, the first device is navigation and the second is the sonar, and in file 2 the first device is sonar and the second navigation, it will detect that and swap them

## Slide 96: Stage 1
Stage 1: View and Options
Heading Window: Smooth heading
Navigation Window:
Smooth position
Remove bad positions
Towfish Altitude Window:
Review and edit bottom detection
Smooth and adjust bottom detection
Note: | Adjustments to the file will be used in mosaicking process. Saving these adjustments to an HS2 file will allow you to re-load the files with adjustments already done

## Slide 97: Stage 1: Heading and Tracklines
Stage 1: Altitude and Heading data
Heading
Smooth heading with
Tracklines
Remove navigation spikes with
Click and drag to select a section of line, then:
  Delete positions with
  Hide imagery with
Notes: Positions can be selected or excluded for smoothing
Areas can also be selected to exclude from the final imagery
Right-click -> Show Charts
97

## Slide 98: Stage 1: Bottom Tracking
Stage 1: Bottom Tracking
Towfish altitude view. The blue line should closely follow the bottom
Choose port or starboard
Use Auto Bottom Detection
    Set a blanking, gate size, sensitivity
    Click Apply
Use the Digitize button to manually set the bottom
Use the Smooth button to smooth the altitude
Use the Up/Down arrows to move the altitude up or down slightly
Note: | Gains are not applied in stage 1
Notes: 98
Blanking: How much of the swath to ignore. Move your mouse to the highest point where imagery appears and copy the Range (near the top) into the Blanking field.
Gate Size determines how much above or below the last ping’s altitude to look for the current ping’s altitude. If no altitude is found in the gate, it will ignore the gate and find a new altitude.
Sensitivity: Higher sensitivity will use samples with lower returns for the bottom, while lower sensitivity will use samples with a higher return for the bottom. Generally, high sensitivity will return a higher altitude than low sensitivity.
Digitize: Click to enter “digitize mode”. Click on the imagery to set the altitude. When finished, click the digitize button to exit digitize mode and set the altitude.

## Slide 99: Stage 2 and Adjusting the Image

## Slide 100: Stage 2
Stage 2: Features & Options
Apply gains and color adjustments
Create targets
Export data to spreadsheet
Save non-georeferenced image
Adjust layback
Notes: 100

## Slide 101: Stage 2: Bottom Tracking
Select Digitizer tool
Click along bottom
Reselect Digitizer tool to apply

## Slide 102: Sidescan Controls - Colors
Right-Click -> Sidescan Controls, View->Sidescan Controls, or Shift + F9

## Slide 103: Sidescan Controls - Gain
Basic Gains: Not recommended
Auto TVG: “Smart” TVG
  Higher sensitivity = brighter image
  Across-Track Smoothing smooths gain
dBs / 100 Meters: dB multiplier
Formula: Applies shown formula
  ‘r’ is range
Angle-Varied Gain: Geocoder gain

## Slide 104: Sidescan Controls - Display
Blank Imagery Adjacent to Nadir: Blanks imagery at given range from nadir

## Slide 105: Stage 2
Saving Image as BMP file
Save a non-georeferenced image of entire waterfall
Notes: 105

## Slide 106: Stage 2: Spreadsheet
Spreadsheet Options
Set-up dialog box
Note: Use Tools->Adjust Layback to modify layback for entire file
View->Spreadsheet if not visible
Displays information for each ping
View->Options (or F9), Spreadsheet tab
  Add/remove columns
Output data to a single file or multiple files
Use to adjust Layback for individual pings
Notes: 106

## Slide 107: Stage 2: Coverage
Saving Coverage as TIF file
Current view in display is bounded by blue box
Display coverage of all tracks, background charts & soundings
Current view in display is bounded by blue box
Notes: 107

## Slide 108: Targeting

## Slide 109: Stage 2: Targeting
Select Target (double left-click on feature)
Target window opens
Double-click to mark target
Sliders at top are used for measurements
Click camera icon, click and drag to create image
Notes: 109

## Slide 110: Stage 2: Quick Targets
Bulls-eye icon:
Select, then click to mark target
Shift-right click to remove a target
Options available to adjust targeting
Images saved to “Side Scan Images” folder in shell

## Slide 111: Target Viewer
Tools->Target Viewer
Edit previous targets
Export to RTF file

## Slide 112: Target Classification
Target Classification Database
Select classification from dropdown
Use the ? to open the comparison window

## Slide 113: Target Classifications
Target Classification Database
Launch from HYPACK->Side Scan-> Target Classifications
Create/Edit/Delete a classification
Add/Delete a reference image
Scroll through existing images
How “confident” you are an image belongs to this classification (0-7)
Notes: 113

## Slide 114: Stage 2: Comparing Targets
Using Coverage Map to Manage Targets
Blue target = previous line
Red target = current line.

## Slide 115: Stage 3: Mosaicking

## Slide 116: Stage 3
Stage 3: Side Scan Mosaic
Notes: 116

## Slide 117: Mosaicking Process
Stage 3: Mosaic
Select files to mosaic
Enter resolution
Select Overlap & Filter methods
Single TIFF or one per line
Use Border file for specific area mosaic
Name the TIFF file
“Make Mosaic”
Notes: 117

## Slide 118: Blanking the Nadir region for Mosaic
Ignore a certain distance from nadir
Area adjacent to nadir can often have poor imagery
Useful when lines overlap

## Slide 119: Resolution Calculator
Useful for choosing optimal resolution
Enter your sonar properties
Can be saved to apply later
On close, resolution is set automatically

## Slide 120: Mosaic Filters
Mosaic Filter Options
AVERAGE:
Smooths the mosaic by setting each pixel to the average of the 3x3 pixel neighboring cells.
SHARPEN:
Sharpens the mosaic by enhancing pixel contrast relative to a 3x3 pixel neighboring cells.
MEDIAN:
Smooths the mosaic while preserving edges by setting each pixel to the 3x3 median value.
Notes: 120

## Slide 121: Saving, Batch Mosaicking, and Merge Mosaics

## Slide 122: Saving Your Data:
Data can be saved as:
  HS2 – All settings (gain, bottom track, navigation editing) are saved.
  XYIntensity – Each point will have an intensity value.
  Export to XTF – For non-HYPACK programs.

## Slide 123: Auto Mosaic
Batch Mosaicking
Run SIDE SCAN MOSAIC (HYSCAN) all the way to Stage 3.
Enter all settings and then select “Add to Batch File…”.
Close SIDE SCAN MOSAIC program without generating the mosaic.
When you are ready to make a mosaic, run SIDE SCAN AUTO MOSAIC
Notes: 123

## Slide 124: Merge Mosaics
Merge Mosaics
Run SIDE SCAN MOSAIC (HYSCAN).
Generate a separate mosaic TIF for each file.
Run SIDE SCAN MERGE MOSAICS to combine the separate TIFS into a single TIF.
TIFF
TIFF
TIFF
TIFF
TIFF
Line 1
Line 2
Line 3
Line 4
Line …..
SIDE
SCAN MOSAIC
SIDE
SCAN MERGE MOSAICS
TIFF
Separate TIFF File for Each Survey Line
Single TIFF File Composed of All Individual TIFF Info
Notes: 124

## Slide 125: Thank You !
HYPACK on Youtube.com ( Historical Sessions ) HYPACK Live Chat
HYPACK on Youtube.com ( Newer Sessions ) HYPACK Ustream
HYPACK SUPPORT Site HYPACK Website
Links to more information:
Contact Us:
Sales@HYPACK.com
Help@HYPACK.com
(860) 635 - 1500