## Slide 1: MBES – Data Collection

## Slide 2: HYSWEEP® Overview

## Slide 3: HYSWEEP® Overview
S/V Bufe - USACE Sault Ste. Marie Area Office
Full Coverage Survey of a DC3.

## Slide 4: Multibeam vs. Single Beam
The Good:
Saves time: Multibeam provides high resolution and full coverage of the seafloor. The data is more accurate for volume computations.
The Bad:
More data to work with but takes more time to process. With additional sensors needed, there are more error sources.
Example of using a Multibeam where previous work was with single beam sonar. An Obstruction was easily missed
The Ugly:
Plane is lost entirely in singlebeam contours.
Multibeam
Singlebeam

## Slide 5: Multibeam Sonar Types
Beamforming Systems:
Forms beams using an array of transducer elements.
Each beam has a Maximum Response Angle, giving the direction of the beam.
Interferometric Systems:
AKA ‘bathymetric sidescan’.
Forms beams from phase angle of backscatter.
Multiple Transducer Systems:
Widely spaced Singlebeam transducers pointing down.
Seabat T50-P
Edgetech 6205
Ross Sweep System
ADCP Systems:
Angular-set transducers
SonTek M9
CAATI Systems:
Computed Angle-of-Arrival Transient Imaging.
PING 3DSS-iDX-450
Notes: 5

## Slide 6: Support Sensors
Heading: Using a gyro or dual GPS antenna array.
Motion reference (MRU / IMU):
Measures boat heave, pitch and roll.
Sound Speed Sensor & Profiler:
Sensor: Sound speed at sonar head.
Profiler: Sound speed through water column.
Notes: 6

## Slide 7: HYSWEEP® MB Interfaces
Atlas: Bomasweep, Fansweep, Hydrosweep MD2, MD/30, MD/50, DS.
Benthos: C3D.
BlueView: MB2250/1350, BV5000.
EdgeTech: 2205, 4600/6205.
Furuno: HS Series.
GeoAcoustics: GeoSwath.
Ibeam Multibeam
Imagenex: Delta T, DT100/101 SIR, Dual Delta T
IS Tech Multibeam
Kongsberg: MS1000, M3
Klein: 5000, Hydrochart 3500
Norbit: WBMS single and dual head, WINGHEAD
Odom: ES3, Dual ES3, Echoscan II, Miniscan, MB1 (dual), MB2 (Dual)
Picotech: PicoMBES
Ping DSP: 3DSS-DX, 3DSS-iDX
R2Sonic: SONIC 2020, 2022, 2024, 2026 (Dual – All).
Reson: Seabat 71xx, 81xx, 900x, T20P, T50P/R (Dual – All)
Ross: Smart Sweep.
SEA: Bathyswath, SWATHplus.
Seabeam: 2100, SB1000 Series, 3000 Series.
Simrad (Kongsberg): EM 302, 710, 1002, 2000, 2040(c), 2040 Dual Head, 3000, 3002, 3002 Dual Head, SM2000, ME70 (ALL & KMALL formats)
SonTek: M9 HydroSurveyor
Tritech: SeaKing.
WASSP: Multibeam, DRX
Multibeam Sonars Available in HYSWEEP®:
At last count, 50 different multibeam and multiple transducer systems are supported.
Notes: 7

## Slide 8: HYSWEEP® Topographic Lasers
2G Robotics ULS-500
Leica: P20/P15/P30/P16, P40, P50
Newton Laser (Beta)
Optech: ILRIS, Polaris
Ouster OS-1
Quanergy M8 Beta (Horizontal & Vertical)
Renishaw/Carlson: Dynascan & Merlin
RIEGL: LMS and V Series, miniVUX
Trimble: MX2
Velodyne: VLP-16 (Hi Res)/32, HDL-32E
Laser Scanners:
REIGL V-Series
Renishaw Merlin
Velodyne VLP-16
Notes: 8

## Slide 9: HYSWEEP® Driver Reference
Advanced Navigation: Spatial, Spatial Dual, Spatial FOG Dual, etc.
AML: AML-3, AML-6
Applanix: POS/MV, (Ocean, Wave, and Surf Master Models).
Coda Octopus: F180.
IXSEA: OCTANS, PHINS, Hydrins.
JAE: JM7531.
KVH: Gyrotrac.
Novatel: SPAN
Odim: MVP (Moving Velocity Profiler - HYPACK Survey driver).
SBG: Ellipse, Ekinox and Apogee Models
Seatex: MRUx.
SG Brown: 1000S.
Sontek YSI Castaway
TSS: 335B, DMS.
Valeport: Swift CTD.
*** - Other sensors available via the generic and NMEA drivers.
Motion / Heading / Other Sensors:
Sontek Castaway
CTD/SV Probe
AML AML-3
CTD/SV Probe
Valeport Swift CTD/SV Probe
Notes: 9

## Slide 10: Installation
Motion Sensor: Mount at boat CG. Alternate location: As close as possible to boat CG.
Integrated MRU at the Sonar is becoming commonplace.
Sonar mounting (in order of preference for data quality):
Hull mount at boat CG
Moon pool at boat CG
Pole mount; bow or over the side
Hull Mount
Pole Mount: Bow
Pole Mount: Over the Side
Moon Pool
Notes: 10

## Slide 11: HYSWEEP® HARDWARE

## Slide 12: Sensor Interfacing
Bringing in the data
Network: For high volume data like multibeam. Data is received with UTC time tag.
Serial RS-232: For lower data volume like GPS.
Time Tagging
Very Important - Device data are correlated by time tags.
All devices must use the same time base – UTC time or PC time.
Without it, data will not be good
Typically, Motion and Heading messages do not contain time tags. Data gets timed at arrival to COM port.
Exception is GPS ($GPGGA has a UTC time tag) and Inertial Systems (embedded time tag in data packet).
Network and COM inputs
POS
POS
MB
MB
MB
MRU
MRU
MRU
MRU
+ time
Asynchronous data are correlated with time tags.
Notes: 12

## Slide 13: Do I Need to Synch My Clock to UTC?
If you have a Positioning device that sends datagrams with UTC time stamps, AND devices that do NOT have embedded UTC time stamps, then the answer is:
Yes
Examples of when time synch to UTC is required:
GPS (UTC), Seabat (UTC), TSS DMS/05 (No time sent), Gyro (No time sent).
POS/MV (UTC), Seabat (UTC), Single beam on a COM port (No time sent).
Time Synchronization by GPS ZDA ONLY = +/- 10 – 30 mSec in Latency, however, it can be improved to
+/- 1 – 5 mSec in Latency by using a HYPACK 1PPS Box.
Notes: 13

## Slide 14: Reson Seabat 7125
HYPACK®/ HYSWEEP® Computer
POS/MV Inertial System
Seabat 7125
Position, Time Sync, Heading, Motion
Groups (3,7,10,20,102)
Multibeam Data
HYPACK does NOT require 1PPS
Motion
Key
RS-232
Network
BNC (1 PPS)
1 PPS
Time Sync (ZDA)
Note: HYSWEEP.dll is not required.
However, can still be used to share motion and heading information with the SURVEY program. Without this driver the SURVEY, the NADIR Depth of the MB and the time series plot of motion data will be unavailable.
Notes: 14

## Slide 15: Kongsberg EM3002
Time-tagged Sonar, Heading & HPR
HYPACK®/ HYSWEEP® Computer
Key
RS-232
Network
BNC (1 PPS)
HYPACK does NOT require 1PPS, but using 1PPS is recommended
Position (GGA) Time Sync (ZDA)
GPS
Heading & HPR
Kongsberg EM3002
Note: HYSWEEP.dll is not required.
However, can still be used to share motion and heading information with the SURVEY program. Without this driver the SURVEY, the NADIR Depth of the MB and the time series plot of motion data will be unavailable.
Notes: 15

## Slide 16: R2Sonic with 1PPS Box (example)
HYPACK requires time sync shown with the optional PPS box.
HYPACK®/ HYSWEEP® Computer
Sonar Data
Key
RS-232
Network
BNC (1 PPS)
Position (GGA)
Speed (VTG)
Time Sync (ZDA)
R2Sonic 2022/2024
Heading
TSS DMS/05
(HPR)
Motion (TSS)
1PPS Box
GPS w/heading
PPS
To aid Motion (HDT, VTG & GGA)
Note: HYSWEEP.dll is not required.
However, can still be used to share motion and heading information with the SURVEY program. Without this driver the SURVEY, the NADIR Depth of the MB and the time series plot of motion data will be unavailable.
Notes: 16

## Slide 17: Reson 8101 with 1PPS Box:
HYPACK requires time sync and shown with the optional PPS box.
Time Sync
HYPACK®/ HYSWEEP® Computer
Sonar Data
TSS DMS/05
(HPR)
SG Brown Gyro
(HDT)
Key
RS-232
Network
BNC (1 PPS)
GPS
1PPS Box
Position (GGA) Time Sync (ZDA)
Seabat 8101
Aiding
Note: HYSWEEP.dll is not required.
However, can still be used to share motion and heading information with the SURVEY program. Without this driver the SURVEY, the NADIR Depth of the MB and the time series plot of motion data will be unavailable.
Notes: 17

## Slide 18: NORBIT iWBMS
HYPACK®/ HYSWEEP® Computer
NORBIT iWBMS
(w/ integrated IMU)
Position, Time Sync, Heading, Motion, Tide
Multibeam Data
HYPACK does NOT require 1PPS
Note: HYSWEEP_Extended.dll can also be used to ‘share’ Position, Tide, Motion, Heading and Nadir Depth information with the SURVEY program. Primarily for Dredge Monitoring.
Not recommended for detailed surveying or precise timing.
Notes: 18

## Slide 19: Offsets
Adjustment for:
Boat Origin (AKA Reference Point): Vessel Center of Gravity XY. Static waterline Z.
Device Location: Offsets in X (Starboard), Y (Forward) and Z (Vertical), as measured from boat origin.
(Be aware that X and Y are reversed in most Inertial systems)
Device Rotation: Pitch, Roll and Yaw orientation of directional devices such as multibeam sonar.
Device Latency: Time delay = data arrival time – data valid time.
Tracking Point: XY location of the sonar head. Used to adjust the Left/Right indicator.
HYPACK HARDWARE – Boat - Mobile
“Red Rogers” and drawing (device locations).
Notes: 19

## Slide 20: Boat Origin & Tracking Point
In this example, the MRU is at boat origin, tracking point is over the transducer.
MRU
MRU
Multibeam TRANSDUCER
Multibeam TRANSDUCER
+X
+X
+Y
+Z
Boat Reference System
Tracking Point
Notes: 20

## Slide 21: HYPACK® Hardware
Combined Hardware program will set the hardware for both HYPACK® and HYSWEEP®.
System Tab:
  Include HYSWEEP Survey
Main page:
  Configure HYPACK SURVEY (Boat) devices and then HYSWEEP SURVEY devices

## Slide 22: HARDWARE (HYPACK® SURVEY)
Positioning Devices (Heading and RTK Tide, as needed):
GPS.DLL (just about any make and model) COM Port or Network
ADVANCEDNAVIGATION.DLL (ANSS INS Systems) Network
POSMV.DLL (Applanix INS Systems) Network
F180.DLL (CODA F-series INS Systems) Network
HYSWEEP_EXTENDED.DLL (NORBIT INTEGRATED INS Systems) Network
IXSEA.DLL, PHINS.DLL, OCTANS.DLL (iXBlue/iXSEA INS Systems) Network
SEAPATH.DLL (Kongsberg INS Systems) Network
NOVATEL.DLL (Novatel INS Systems) Network
SBG.DLL (SBG INS Systems) COM Port or Network
SONARDYNE.DLL (Sonardyne INS Systems) Network
VECTORNAV.DLL (VectorNav INS Systems) Network
Select ‘Time Synch’ option on the HYPACK configuration page (as needed).

## Slide 23: HARDWARE (Configure HYSWEEP®)
Configure the HYSWEEP® Survey section for:
Multibeam, Motion sensor and Heading.
Select from Manufacturer/Model list and “Add” to the INSTALLED section.
Note: Some multibeam systems may include MRU and Heading within their driver
No HYPACK® Navigation device under the HYWEEP Survey section.
It is automatically included in the Hardware program.
Notes: 23

## Slide 24: Multibeam Device
Connect:
Most sonars are network. (Enter the correct Port # and Internet Address, if not correctly defaulted)
TCP/IP devices ‘require’ the specific IP Address
Refer to “HYSWEEP Interfacing.pdf” for details (C:\Hypack 20xx\Documentation)

## Slide 25: Multibeam Device – Offsets Tab
Select Sonar Head 1 or 2.
Enter Location offsets (Starboard, Forward, Vertical) as measured from Boat Reference Point.
Enter Rotation offsets (Yaw, Pitch, Roll) from Patch Test.
Latency should be 0.00.
(Navigation Latency is entered in the Positioning Device’s Offsets)

## Slide 26: Multibeam Device – Offsets Tab (continued)
For multibeam sonars that include the Motion Sensor data embedded in their data packets, select MRU Offsets from the pulldown menu:
Enter Location offsets (Starboard, Forward, Vertical) as measured from Boat Reference Point.
Enter Rotation offsets (Yaw, Pitch, Roll) from Patch Test.
Latency should be 0.00, unless otherwise stated by the manufacturer.

## Slide 27: Motion and Heading Sensors
Devices:
Select the driver, if listed. If not…
  The “TSS1” message is standard for Heave, Pitch and Roll (TSS DMS driver).
  The NMEA “HDT” message is standard for Heading (NMEA-0183 Gyro driver).
  The Generic Attitude driver can be configured to parse ASCII datagrams
Connect:
Enter Network or COM settings. (Consult the “HYSWEEP Interfacing.pdf”.)
Offsets:
MRU Location offsets measured from boat reference.
MRU Rotation offsets can be used to “zero” Pitch and Roll.
(https://www.hypack.com/File%20Library/Resource%20Library/Technical%20Notes/11_2017/HYSWEEP-Angular-Offsets---Static-Pitch-and-Roll.pdf)
Heading Rotation (Magnetic Declination) offset (Yaw) can be used to correct to Grid North.

## Slide 28: Testing and Saving…
CONNECT Tab: Use COM Test and Network test to verify sensor is sending data
Alternate Hardware Configurations:
Open and Save alternate configurations using the IMPORT and EXPORT
Notes: 28
I have a note about saving the changes. Last year’s slide says to save the changes [meaning click the Yes button when the prg asks to save changes] and gives the full path to the Hysweep.ini. That seems more clear/exact. There was a note on that slide [changes saved to Hysweep.ini] but this is another I don’t remember what he wanted different.

## Slide 29: Calibration Tools
HYSWEEP® Patch Test
Roll, Pitch, and Yaw angular alignments.
Determine the orientation of the sonar, with respect to the MRU and Heading devices.
Account for GPS Latency, if needed.
HYSWEEP® Bar Check
Much like single beam - verify draft measurement.
Multibeam systems need calibration!
Why we need to Patch test.
Bar check window.
Notes: 29

## Slide 30: HYSWEEP® SURVEY

## Slide 31: HYSWEEP® Survey
Multibeam Survey Program
Collects and logs multibeam and support sensors.
Displays are Real-time corrected and provide QC info.
For Simulation and Survey Practice:
https://www.hypack.com/File%20Library/Sounding%20Better%20Newsletter/2014/MB-Simulation_Playback_Automtx.pdf

## Slide 32: HYSWEEP® Survey
Survey Preparation:
Geodetic parameters and HYPACK® and HYSWEEP® hardware configuration
Planned lines or matrix for navigation
Pre-set TPU parameters in the TPU EDITOR if you want to use Total Propagated Uncertainty
Create Sound Velocity and Tide file to be used during survey
Launch Survey:
Use menu to run HYPACK® SURVEY and HYSWEEP® SURVEY together.
Use Smart Launch icon to run both.
TPU setup

## Slide 33: Survey Preparation
Planned Survey Lines
Make parallel lines spaced for target coverage.
Sometimes difficult with multibeam, as coverage changes with depth.
Coverage Matrix
Alternative to planned lines.
“Mow the Grass” and ‘paint the bottom’ to assure proper overlap and 100% ensonification is achieved.
Large depth changes make line planning difficult. Alternative is “Mowing the Grass”.
Notes: 33

## Slide 34: HYSWEEP® Survey
Features
Data collection and logging.
Targeting and coverage mapping.
TPU and other QC checks visible in over 30 real time displays
Refraction Errors seen in real time
Refraction occurs at changes in sound velocity.
Errors when SV profile doesn’t match conditions – estuaries can be troublesome.
Look for ‘smiling’ or ‘frowning’ sweeps.
Same take-off angle, different ray paths.
HYSWEEP® 3-D Seafloor
Notes: 34

## Slide 35: Multibeam Auto Processing
Launch Auto Processing before data collection begins, preferably before launching SURVEY.
Yes: Use this first time to select devices and setup filters.
No: Use when there are no changes in device or filter settings.
Yes: Loads, filters and saves survey files on end logging. Resets memory for the next file.
No: As above except files are retained in memory for coverage mapping.
Allows surveyor to ‘set’ pre-filtering processing parameters, so that a preliminary, Final data set can be ready, immediately after the Survey has been collected.

## Slide 36: HYSWEEP® Main Window
Alarm Indicators
Green = OK.
Yellow = Something’s not right here.
Red = Look Out!
(Click on the ‘button’ to read the Alarm details)
Various system measurements updated once a second.
Data Filename or “Offline” in title area.
Select Boat or Towfish for display of sensor data.
Typical Alarms:
Devices: Timeout, COM or Network port open error, checksum error.
QC: Heave drift, SV profile no longer valid (doesn’t match the sensor).
Notes: 36

## Slide 37: View Options (F9)
Set Depth and Angle Limits.
Important NOTE: The ‘View Options’ ONLY affect the ‘display of the Real Time data’. It does NOT affect the ‘actual data’ that is being collected. Even if you incorrectly set one of these options, you will NOT affect the data being stored in the files.
Select Different Window Displays.
Select and Set Different QC Tests and Alarms.
Notes: 37

## Slide 38: View Options (F9) (Continued)
Select which Coverages to Display.
Select which corrections to apply in Real Time.
Select and Set Different Laser Filters
Important NOTE: The ‘View Options’ ONLY affect the ‘display of the Real Time data’. It does NOT affect the ‘actual data’ that is being collected. Even if you incorrectly set one of these options, you will NOT affect the data being stored in the files.
Notes: 38

## Slide 39: HYSWEEP® Survey (over 30 Display windows)

## Slide 40: Profile and 3-D Seafloor
Profile Window
Single sweep from aft looking forward.
Color coding can be based on beam quality.
Useful QC.
Swath Width at top.
User defined scale for depth and swath
3-D Seafloor Window
Styles: Wire frame + solid / color TIN
Individual Sounding Points
Mouse targeting and measurement.
Great tool for bottom visualization.

## Slide 41: Waterfall Windows
Multibeam Waterfall
Color or solid TIN display.
Good for visualization, targeting and comparison to sidescan.
Intensity Waterfall
Imagery. No depth info.
Average backscatter (one sample per sounding) or snippets (many samples).
Apply TVG Gains
Sidescan Waterfall
Sidescan data from the multibeam.
Full image control; colors, gains, bottom tracking, etc.

## Slide 42: Interferometry
Processing the raw data from interferometry (bathymetric sidescan) systems
Select from many raw data filters. For example:
  Filter by Intensity: Simple filter - rejects data outside intensity limits.
  Filter Along Track: More complex – gating filter based on along track history.
Select beamforming method and settings
  Bin size and Max Width: Beam footprint and total swath width. Use this to manage file size and edit time.
Alternately, you can use simple downsample and store a maximum of 1440 points per ping - very large files.
Interferometry Window: Combines filter limits, raw data and beams.
Notes: 42

## Slide 43: Laser Scanner Data (Topo)
Inside HSX data is stored in new message type (TOP)
Can run concurrent with a multibeam sonar
Works with Velodyne, Optech, Leica, Carlson/Merlin, RIEGL and more

## Slide 44: HYPACK® Real Time Cloud
Fully corrected – sound speed, tide, motion, etc.
Simultaneous Multibeam + Topo Laser data.
Selectable 3D boat shapes
User defined number of points, (default is 4,000,000)
Tiltable and Rotatable
Take ‘still shot’ BMP’s
Create Targets of objects
Measure between points

## Slide 45: HYSWEEP® SURVEY QC Tests
QC Test Window
Select from four test displays.
“Std. Deviation by Beam” is a nice estimation if the bottom is reasonably flat.
Some Useful Alarms
Heave Drift: Alarm if average heave exceeds threshold.
SV Profile Minus Sensor Difference: Alarm if difference exceeds threshold.
Evidence of heave drift.
Min/Max Sonar SV Probe Limits
(Warning that your Probe may be fowled with debris or reading a significant SV change)
Notes: 45

## Slide 46: TPU – What is it?
Total Propagated Uncertainty
A method to account for all sources of measurement uncertainty in a sounding
  Echosounder uncertainties
  GPS accuracy
  Motion sensor accuracy
  Offset measurements
  Sound velocity profile corrections
Three major components
  TVU – Vertical only
  THU – Horizontal only
  Target Detection Size Limit
    Smallest target that can reliably be detected
Hare, Rob. "Depth and Position Error Budgets for Multibeam Echosounding." The International Hydrographic Review 72.2 (2015).

## Slide 47: TPU in Real Time
In real time, HYSWEEP® SURVEY can display graphs of the Depth and Position Uncertainty, along with the Minimum Target Detection Size.
Non-compliant soundings can be excluded from the coverage matrix

## Slide 48: TPU Windows
Select survey criteria
Parameters are entered in the HYPACK SHELL under:
  EDITORS – TPU Editor
Based on the TPU Parameters and real time sounding info, you can calculate and display:
  Total Sounding Uncertainty (Vertical)
  Total Positioning Uncertainty (Horizontal)
  Target Size Limit Value
Can display against:
  IHO Special Order Requirements
  IHO 1st Order Requirements
  USACE Hard Bottom Requirements
  USACE Soft Bottom Requirements

## Slide 49: Coverage Map
Show Multibeam Coverage Four Ways
Multibeam Coverage in HYSWEEP®: Fast and easy ‘stick’ plot. No setup is required. Great for showing overlap.
Filled matrix in HYSWEEP®: Cut cross sections through the matrix and track overlap QC.
User-defined matrix in HYPACK®: Overlay on background files. No sections or QC.
Auto matrix in HYPACK®: Automatic matrix creation in HYPACK SURVEY. No need to create a Matrix before starting survey. MTX files will only be shown in HYPACK SURVEY.
(Use View Options and Matrix Options to configure the coverage map.)
(1) HYSWEEP® Coverage
(2) HYSWEEP® Filled Matrix
(3-4) HYPACK® Filled Matrix
Notes: 49

## Slide 50: Other Windows (ENLARGE SCREEN CAPS)
Nadir Depth 1 and 2
Distance between your expensive sonar head and the bottom - turns RED when too shallow.
Time Series:
Track Heave, Surface SV and RTK Tide in Real Time. Great for showing problems, as they happen.
Shore View
Laser scanner topographic display.
Graphical HPR:
Heading, Pitch, Roll and Heave. Cockpit style display.
Notes: 50

## Slide 51: Corrections
Sound Velocity
Type in depth and sound speed data or,
Import the profile from file or
Receive automatically from MVP.
The profile is applied in Survey for real time QC. Also saved for post-processing.
Squat and Settlement
Enter a table of draft adjustment vs. speed.
Draft lookup is based on speed over ground, which does not account for current
HYSWEEP® Sound Velocity Editor
SONTEK CASTAWAY SV Probe. Simplified Bluetooth Upload.
Notes: 51

## Slide 52: Logging Data
HYPACK® Commands
Ctrl-S to Start, Ctrl-E to End logging.
Data logged to ASCII *.HSX file by HYSWEEP® Survey.
Two Data Files per Survey Line
Same root name (e.g., 002_1116), different extension (HSX and RAW).
HSX logged by HYSWEEP® Survey: All data required to process multibeam. Offsets, soundings, positions, motion and heading data, tide, draft, SV …
RAW logged by HYPACK® Survey: Navigation and detailed position information.
Logging Options
File Overlap to avoid gaps between files..
Custom Logging folder selection.
TOP message. For logging > 1440 shots per topo laser scan.
Notes: 52

## Slide 53: HYSWEEP® Bar Check
Setup
+/- Depth Gate: Soundings outside bar depth +/- the gate are ignored.
+/- Angle Limit: Soundings with beam angle outside limits are ignored.
Running The Test
Run Bar Check from the Tools menu.
Click “Reset Barcheck.txt” to clear the report.
  Lower the bar and enter Bar Depth.
  When Measured Depth stabilizes, click “Save Depth”.
  Repeat for each bar depth.
  Adjust Sonar Draft if needed.
When done, click “Barcheck.txt” to view or print the report. Option to save Sonar Draft to HYSWEEP.INI on exit.
Bar Check averages depths for three seconds then saves and graphs the result.
Important NOTE: Takes Pitch and Roll of the Vessel into account, which is why the ‘Pitch Average’ and ‘Roll Average’ are displayed, so that you can figure out what ‘Offset values’ to plug into Hardware, for the MRU device.
Notes: 53

## Slide 54: HYSWEEP® Playback
HYSWEEP® SURVEY can replay HSX files by clicking ‘File – Playback’

## Slide 55: HYSWEEP® Water Column

## Slide 56: Water Column Data
Multibeam Backscatter Throughout the Water Column.
Use HYSWEEP® Water Column Logger to log the data.
Playback Program for quick replay and exam.
You can re-digitize soundings in MBMAX64.

## Slide 57: Hardware Configuration
HYPACK® Hardware Setup
Water Column is Supported for R2Sonic, Reason, and NORBIT Multibeam Systems.
Configure Sonar for Normal Bathymetry then,
Check the Box in Driver Setup.
Logging File Types:
R2Sonic: *.R2S
Reson, NORBIT: *.7K

## Slide 58: HYSWEEP® Water Column Logger
Logger Runs Automatically with HYPACK® and HYSWEEP® Survey.
Real Time Display and Color Configuration.
Continuous and On Demand Logging.
Alarms. (For Example; Low Disk Space)
Typical Data Rate = Two Giga Bytes per Minute.

## Slide 59: WC Logger – Color and Display Settings
Amplitude Graph: Backscatter Amplitude of the Nadir Beam.
Graph Max: Set scale limit of the amplitude graph.
Color Max = Color Saturation Limit: Any amplitude > this setting is shown in Red.
Dot Size: Of individual samples.
Soundings: Check this to overlay soundings in white.
Click and Drag the Blue Bar to quickly change the Color Saturation limit.

## Slide 60: WC Logger – Ping Buffering
Find this in Logging Options
Number of seconds of WC data saved in program memory.
Gives the surveyor some leeway with On Demand Logging.
Equals the number of seconds between (1) spotting a feature and (2) clicking the Logging button.
Pings per Second: Filled in by program.
Bytes per Ping: Filled in by program.
Buffer Size (MB): Entered by the surveyor.
Buffer Time in Seconds: Calculated by the program.

## Slide 61: WC Logger – Data Logging
Automatic Mode
WC Logging mirrors HYPACK® Survey.
On Demand Mode
Only Logs areas of interest.
HYPACK® Start / End Logging
WC Logging Button

## Slide 62: Water Column Playback
Quick survey review.
Play / Pause / Fast buttons and shortcut keys.
Display setup like WC Survey.
Thumbnail map for referencing.
HYPACK® Targets.
Flag points for MBMAX64 editor search.

## Slide 63: Thank You !
HYPACK on Youtube.com ( Historical Sessions ) HYPACK Live Chat
HYPACK on Youtube.com ( Newer Sessions ) HYPACK Ustream
HYPACK SUPPORT Site HYPACK Website
Links to more information:
Contact Us:
Sales@HYPACK.com
Help@HYPACK.com
(860) 635 - 1500