## Slide 1: SBES – Preparation

## Slide 2: Physical Offsets
GPS
Sonar
Frequently the GPS and the Sonar are not located at the same horizontal position
A reference point needs to be selected and all offsets measured to that point.

## Slide 3: HYPACK HARDWARE

## Slide 4: HYPACK® Hardware
HYPACK HARDWARE, HYSWEEP HARDWARE & SIDE SCAN HARDWARE are all configured from this program.

## Slide 5: HYPACK Configuration Page
If you have a multibeam device, check the “HYSWEEP Survey - Include” box. If you have a Sidescan, check the “Sidescan Survey - Include” box. If you have both, check the “HYSWEEP Survey - Include” and configure both of them under Multibeam.
Right-click on ‘Hardware’ to add another mobile.
For multibeam, check “Include”. This creates a ‘HYSWEEP Survey’ listing. Then click on the listing to add you multibeam, MRU and gyro systems.

## Slide 6: Vessel Page: Mobile Tab
You can name each vessel.
Specify the Tracking Point for each mobile. This is the point used to determine the distance off-line, distance to-go, etc.
Specifying tracking points in Survey gives you more flexibility!

## Slide 7: Vessel Page: Survey Devices Tab
This is where you go to specify the devices used on each mobile.

## Slide 8: Vessel Page: Vessel Shape Tab
You can visually inspect the location of your sensors and pick your default 2-D boat shape for HYPACK SURVEY.

## Slide 9: Devices: Survey Devices Tab
Click on a vessel to add devices.
Click on an installed device to access the functions, options and setup for each device.

## Slide 10: Devices: Connect Tab
Click to get the Device Connection
window.
You can examine the serial port
stream from here.
You can test the device from here.

## Slide 11: Devices: Device Offsets Tab
Specify the position for each device, relative to your boat origin. Remember, Z is positive downwards!
You can now visually inspect the location of your sensors in 3D.
Pan, tilt and zoom in/out. User can load 3od shape files.

## Slide 12: Devices: All Offsets
See all your offsets in one page.

## Slide 13: Example Hardware Configurations
Survey vessel with magnetometer installed on towfish with manual layback.
Survey vessel with R2Sonic multibeam installed on the vessel.
Survey vessel with Edgetech sidescan installed on a towfish.
The multibeam and/or sidescan are placed on the main vessel or the towfish mobile depending on the setting in the HYPACK Configuration tab.

## Slide 14: Device Functions and Options
Optional functionality can be selected for certain devices:
  Record raw messages
  Record device specific messages:
    GPS: Records time synch differences
    Echo Sounders: Records acoustic ping for each ping.
  Use of Matrix Update

## Slide 15: Single Beam Echo Sounder Placement:
X
Y
GPS
Transducer
CO-LOCATE GPS ANTENNA WITH SINGLE BEAM TRANSDUCER

## Slide 16: Serial Port Stuff
RS 232: Short Distance (<30m)
RS 422: Longer Distance (>100m)
  You can connect an RS422 device to an RS-232 port.
    TX- to RX and SG to SG
When configuring a COM port, you must define:
  COMn Port number
  Baud Rate How many bits per second (more or less)
  Data Bits How many bits in one ‘word’
  Stop Bits Bit’s tacked on to the end of each word
  Parity Used to detect transmission errors
  Flow control is generally not needed and not desired.

## Slide 17: Network Connections
UDP requires an IP address and separate read/write port numbers
It may be necessary to reset the IP Address for your computer to an address similar to your network device.

## Slide 18: GPS Configuration

## Slide 19: GPS: Setup Window
Synchronization:
Are you using a 1PPS box?
GPS Status Codes:
Standard – NMEA 3.0 (Most GPS units made after 2005)
Uncheck NMEA box to manually set the Code values.
Option to Show Alarm if GPS Status is lost.

## Slide 20: GPS: Setup Window
RTK Tide:
Minimum status:
      Compute for all and correct in post-processing.
  Filter RTK Tide:
      Recommended on dredges.
      Not recommended on survey vessels.
  Alarms:
Maximum HDOP Value: recommended: 4.0
Minimum number of Satellites: recommended: 5
Maximum synch error (ms): recommended: 100
Maximum baseline error:
Used when computing bearing between two GPS.
recommended: DGPS: 2m | RTK: 0.5m
Maximum correction age interval(s):
      Time between corrections from the RTK base station

## Slide 21: GPS: Setup Window
User Modified NMEA Messages:
    RTA (Odom): Used when Odom’s RTA unit is provided time-tagged info.
    POS (CeeScope): Used when position data is delivered by Ceescope.
    RRIO (Reson)
    CV3 (Odom)
    Ping DSP
    Edgetech
    Kongsberg EM
Used sentences:
Only selected desired messages

## Slide 22: GPS: Setup Window
Show debug messages
Ignore Checksum
Use only for heading (OTFGYRO)
Report antenna elevation as depth
Use GPS time when not synchronizing (special configurations only !!!)

## Slide 23: GPS Windows in Survey
HDOP (Green), # of Sats (Blue), Status: (Red)
Sky Plot (Requires $GPGSV sentence)
Error Ellipse
(Requires $GPGST sentence)
RTK Math Window

## Slide 24: Echosounder Setup

## Slide 25: Echosounder: Vertical Offset
Outputting Depth Below Surface (DBS):
Vertical Offset is set to 0.0
1 m
1 m
6 m
6 m
Sounder outputs 6.0m to computer
Sounder outputs 7.0m to computer
R/V DBS
R/V DBT
Correct for the Static Draft (depth of transducer below the static waterline) either in the echosounder (bar check) or in HARDWARE (Vertical Offset). DO NOT USE IN BOTH PLACES!

## Slide 26: Echosounder Configuration: Offsets
Offsets:
Enter the offsets of the echosounder transducer, relative to the boat origin.
Vertical Offset:
If your echosounder outputs the Depth Below Surface, then enter a Vertical Offset = 0.0
If your echosounder outputs the Depth Below Transducer, then enter Vertical Offset = Static Draft.
Z = positive downward!
Latency:
For almost all single beam sounders, enter Latency = 0.00.
Enter the combined latency between the GPS and Echosounder determined in the SINGLE BEAM LATENCY program as the latency for the GPS device.

## Slide 27: Echo Sounder Configuration
Functions:
Available functions may differ, depending on the echo sounder. As a minimum, you want to select ‘Depth’.
Options:
‘Use for matrix update’: Paints a matrix with the color-coded depth data.
‘Paper Annotation’: Enables the output of annotation to the echo sounder at event marks.
‘Record device specific messages’: Enables the storage of acoustic data for certain sounders.

## Slide 28: MRU use in HYPACK

## Slide 29: MRU Decision Tree
I have an MRU.
Is it being used along with a multibeam sonar?
Configure it in HYSWEEP® HARDWARE.
Do you also want to use the HPR values in HYPACK® SURVEY?
Add the HYSWEEP.DLL in HYPACK® HARDWARE
You are done!
You are done!
How is the MRU integrated?
Make sure the ‘Heave’ function for the echosounder is enabled in HYPACK® HARDWARE
Add the device driver for the MRU in HYPACK® HARDWARE.
You are done!
You are done!
Yes!
Yes!
No
No
Through the echo sounder device driver.
Through its own device driver

## Slide 30: Connecting your MRU
Echosounder
MRU
Echosounder
Heave-corrected soundings
Raw
Soundings
HPR Data
HPR Data
You can do it this way …..
We prefer you do it this way.
This is recommended only if your echo sounder can output the raw depth and heave measurement as separate entities.
Select the specific device driver for your MRU and configure it!
If you echosounder can output uncorrected depths and MRU data, then we have no objection!
MRU

## Slide 31: Where to put the MRU?
Try to mount your MRU at the center of mass of your vessel. If you can’t do this, mount it as close as possible to the center and carefully measure the offsets.
MRU
MRU
GPS
GPS
XDucer
XDucer

## Slide 32: HYPACK Timing

## Slide 33: HYPACK® Timing Basics
The internal clock on your computer is a poor time device.
HYPACK SURVEY and DREDGEPACK® use a proprietary clock model called VERITIME.
When you start SURVEY or DREDGEPACK®
  VERITIME is initially set to the Windows clock time.
  VERITIME and Windows clock times slowly drift apart.
In ‘Normal’ mode, all devices receive their time tags from the VERITIME clock model.
  All devices are time tagged off the same time standard.

## Slide 34: Time Tagging
TIME
TIME OF MEASUREMENT
TIME OF RECEIPT OF 1ST CHARACTER
Latency Time of Device
Time of Receipt of 1st Char: 08:32:15.000
Latency Time for Device: 0.200
Time of Measurement: 08:32:14.800
Device drivers monitor a serial/network port. They have the highest priority!
When the 1st character of a message arrives, the program gets a time tag from the VERITIME routine.
To adjust for the delay in transmission from the time of measurement to the time of transmission, a ‘Latency’ correction is entered in the Offsets in HYPACK HARDWARE and is subtracted from the VERITIME time tag.

## Slide 35: Theory of Latency
A 0.5 second Latency error at 8 knots = 6.75’ or 2+ meters Position shift
There is a delay in time from when your GPS computes a position until it is transmitted out the Serial port or Ethernet connection.
If you don’t correct for this Latency, your depths will not be in the correct position.
  In most cases, they will be backwards along the track line.

## Slide 36: Test Survey Lines
For Singlebeam, Run reciprocal survey lines up/down a slope or over a known feature.
  It’s best if your planned lines are perpendicular to the bottom slope!
If the Latency correction is perfect, the profiles will overlay each other.
  If there is an error, the profiles will be early or late.
  The LATENCY TEST program varies the time tags to determine the best ‘fit’ Latency time.

## Slide 37: The Keys to a Good Test
Run perpendicular to the bottom slope.
  Running non-perpendicular to the slope will generate errors unless the reciprocal track-lines are ‘dead on’.
Run the test at slack tide.
  The test does not factor Tide, Draft, Heave, or Pitch corrections.
Keep as close to the planned line as you can.
Watch the GPS constellation.
  No big changes in HDOP during the test.
  You might consider setting your GPS Elevation mask to +20°, so when a new satellite arrives, it won’t jump your position too much. (Set it back after the test!)
Jumps in position due to poor GPS positioning can result in false latency results.
  Run the LATENCY TEST three times, each time with a separate pair of lines and use the average latency time.
  Results are more easily repeated with RTK GPS than with DGPS.

## Slide 38: Before & After Profiles
Before
After

## Slide 39: Setting the Latency in HARDWARE
LATENCY TEST computes a combined value between the GPS and the Echosounder.
In the HARDWARE program for your GPS device:
  Take the current Latency time for the GPS (1.000 in example).
  Subtract the result from the average of 3 LATENCY TESTS.
    (1.00 – 0.75 = 0.25 for this example).
  Set the Latency time of your GPS to 0.25 (for this example).
  Make sure the Latency time of your echosounder is set to 0.00
Now, go back to SURVEY, collect 3 more sets of test lines and check the results.

## Slide 40: Correcting Latency - SINGLE BEAM EDITOR (32 bit)
Correcting Existing RAW Data Files:
  You can update the Latency value used during data collection by changing the value in the SINGLE BEAM EDITOR.
  Enter the correct Latency value as determined in the LATENCY TEST program.

## Slide 41: Correcting Latency - SBMAX 64
In the SBMAX64 editor, enter the latency in the Navigation field on the device offset page

## Slide 42: Clock Synchronization

## Slide 43: Who Should Synchronize?
Synchronize if you have a multi-beam that outputs datagrams with UTC time stamps.
Synchronize if you plan to use post-processed heave.
Synchronize if you plan to use post-processed GPS positions.
Synchronize if you are using LiDAR data

## Slide 44: Preparing your Computer to Synch the Clock
The Synch Clock function requires that the computer be exposed to changes from other programs.
The User Account Controls Notification should be disabled to allow the software to update the computer time.
If this is not disabled, the Veritime Clock will still function, however the computer time will not be changed.

## Slide 45: How Clock Synchronization Works
GPS
WINDOWS
Time
UTC time from the GPS is received using 1Hz ZDA message and optional PPS signal.
Veritime Clock
Using the GPS Time the clock monitored and updated every second. The current time is pushed to WINDOWS to update the computer time.
The device timing uses the VERITIME time for record time. If the time push to WINDOWS fails the device time is still in synch with the GPS time.
The time in the Data Display is the local time representation of VERITIME

## Slide 46: Clock Synchronization: How it works
When the ZDA sentence arrives: (1 Hz only!)
  HYPACK SURVEY compares the UTC time from the GPS (corrected with the time zone offset) with the time from the VERITIME clock model (HYPACK SURVEY).
  It can speed up the VERITIME clock model, or slow it down so that it matches UTC.
  You should wait one or two minutes after starting HYPACK SURVEY before starting to survey to allow the VERITIME clock model to synch to UTC. SURVEY will show a “No Synch” error until it locks on.
When the GGA sentence arrives (any rate):
  HYPACK SURVEY uses the time tag in the GGA sentence (corrected for local time zone offset) as the position time tag.
When a message arrives from your echosounder, MRU or other non-GPS device:
  HYPACK SURVEY gets a time tag from the VERITIME clock model, which has been ‘synched’ to UTC less the local time zone offset.

## Slide 47: Clock Synchronization
Device Message | Veritime Action | Time Tag
‘ZDA’ from GPS | VERITIME Clock Model Adjusted | Difference recorded in RAW record
‘GGA’ or ‘GGK’ from GPS | Nothing | From GGA/GGK sentence
Echosounder, gyro and other devices | Nothing | From VERITIME model
  These times are adjusted to local time zone, along with any latency offset entered by the user and used as the time tag for the position.

## Slide 48: Clock Synchronization – 1PPS Box
Without a 1PPS Box: Time of ZDA sentence is based on the arrival of first character of ZDA transmission.
With a 1PPS Box: Time of ZDA sentence is based on arrival of 1PPS pulse.
GPS
Computer
RS-232 Out (GGA, VTG, ZDA)
GPS
Computer
RS-232 Out (GGA, VTG, ZDA)
1PPS Box
1 PPS Out
RS-232 Out (GGA, VTG, ZDA)
With 1PPS Info on CTS Line
Without 1 PPS Box
With 1 PPS Box
12VDC

## Slide 49: The 1 PPS Box
12VDC In
RS232 Out (to computer)
1 PPS In
(from GPS) BNC Connector
RS232 In Requires ZDA at 1 Hz May also carry 1PPS pulse on Pin 8 or 9
1 PPS Receipt Strobe
Alternates RED/GREEN every 1 second when operating correctly
The use of the PPS box is to allow the computer time to detect the PPS signal.
The PPS box converts a short pulse into a stable, detectable signal.

## Slide 50: Time Synchronization Tests
ZDA Only
ZDA and 1 PPS Box
Make sure you monitor the difference between the VERITIME and GPS clocks!
The difference should be small (<20mSec) and should work its way towards 0.0 after a spike.
If it gets large and stays large, something is wrong, Stop SURVEY.

## Slide 51: Synch the Computer Clock
Select ONE GPS device to use to synchronize the computer clock to UTC in the HYPACK Configuration page.

## Slide 52: 1PPS Configuration
GPS – Setup
Specify if you are using a 1PPS box.

## Slide 53: ZDA – 1PPS Testing: Utilities
Test the consistency of your ZDA message for synchronization.
Located under ‘Utilities – Calibration’ menu item.
Graph shows ‘Sync Error’ in mSecs. Sync Error equals the difference between VERITIME and the time of arrival of the ZDA message

## Slide 54: Planned Line Editor

## Slide 55: Planned Lines Basics
A planned line needs a minimum of two waypoints.
A planned line can have over 100 segments.
Internal segments can be made as arcs by entering the radius for the arc.
Lines can be:
  2D: Only X-Y at waypoints
  3D: X-Y at waypoints and design depth at Distance Along Line
You can survey without Planned Lines. Many multibeam surveys do not use them and rely on a MTX file(s) to ensure 100% coverage.

## Slide 56: Line Editor: Arc Segments
Enter inside (or outside) radius for a segment.
Curved lines CANNOT be used when computing volume quantities.
If the arc is created on the wrong side, add a “-” to the radius to flip it to the other side!

## Slide 57: Offsets: Centerline
Create your centerline, Select Offsets: Centerline, Generate perpendicular lines.
Smart Corners, Centerline Offsets.

## Slide 58: Offsets: Parallel Lines
Enter your initial line.
Select Offsets: Parallel
Generate your parallel lines.
You can now stagger the offsets:
  50m, 100m, 50m, 100m, etc.
For Parallel Offsets, lines are renumbered North to South and West to East.