## Slide 1: Sub-Bottom Data Collection & Processing
HYPACK 2020 Training Event
January 2020

## Slide 2: Introduction
This presentation covers the following topics:
Sub-bottom profiling data collection in HYPACK.
Configuring a National Instruments analog-to-digital device (NI-DAQ) for sub-bottom profiling or side-scan sonar data collection.
Processing data in the Sub-Bottom Processor

## Slide 3: Sub-Bottom Data Collection

## Slide 4: Sub-Bottom Data Collection
Sub-bottom collection and processing is a standard feature of HYPACK®.
Sub-bottom data are recorded to SEG-Y format.

## Slide 5: Sub-Bottom Profiling Systems
HYPACK®
SURVEY
ANALOG SUB-BOTTOM CH-1
SUBBOT.DLL
A/D Box
NI-USB-BNC 6221, 6341 or 6212
SyQwest B2010/SB3510HD
Stratabox
Manufacturer
Control Program
(system dependent)
SUBBOT.DLL
HYPACK®
SURVEY
Innomar SES-2000
EdgeTech 3000
One DLL is used for all systems
GeoAcoustics GeoPulse Chirp
Teledyne Odom Chirp III
Benthos Chirp
Knudsen
Falmouth HMS-622
DIGITAL SYSTEMS
ANALOG SUB-BOTTOM CH-2
ANALOG SYSTEMS
Specialty Devices

## Slide 6
Simple HARDWARE Setup: SUBBOT.DLL
Add a positioning device & SUBBOT.DLL device and select the SBP in the Setup form
Connection settings must match the SBP system
Notes: 6

## Slide 7
Hardware Test Device: EdgeTech Chirp
Do not band pass filter Chirp data
Notes: 7

## Slide 8
HARDWARE Setup for dual SBP’s: SUBBOT.DLL
Use this HARDWARE setup when surveying with two analog systems simultaneously:
Add a positioning device & SUBBOT.DLL device for the first analog SBP system. Rename the device e.g. “Sparker” to avoid confusion.
Add a Mobile with a second SUBBOT.DLL device & TOWFISH.DLL for positioning. Assign this iteration of SUBBOT.DLL to Channel 2 (these data files with be stored as XXXX_XXXX_02.seg. The TOWFISH.DLL position will be stored in this SEG-Y file.
Rename device
Notes: 8

## Slide 9
Complex HARDWARE Setup: SUBBOT.DLL
Notes: 9

## Slide 10
Analog Sub-Bottom Monitor
The Analog Monitor is used to configure the analog settings for generating triggers and for listening for returns.
Each analog Sub-Bottom system will have its own particular settings to maximize the quality of the returns.
When SURVEY is started, the drivers will automatically start Analog Monitor.
Select the “I/O Channels” button and for each field one needs to configure the channel on the NI USB device that the signal is wired to. Each of the Channels can be assigned a custom label or name applicable to the SBP system in use, i.e. “Sparker Signal”.
The default trigger voltage levels of -5V/+5V should generally be used but the voltage levels for Channel 1 and/or 2 need to be set at this time. The recommended signal voltage levels for Pinger/Chirp SBP systems are between -5V/+5V and -2V/+5V depending on the age of the system whereas hydrophone arrays for boomers/sparkers/etc generally output voltages in the -1V/+1V to -5V/+5V volt range depending on the sensitivity of array, the gain on the hydrophone preamp and the reflectivity of the seabed.
Use the default Terminal Mode (RSE) and default channel sample rate except for advanced users.
Notes: 10

## Slide 11
Analog Sub-Bottom Monitor Continued
The voltage values set for Channel 1 & 2 can be considered as a “base gain” for the channel and it is important not to clip the incoming signals as these clipped data cannot be recovered. A Rule of Thumb is to set the voltage range about one third higher than the actual input signal voltage.
Any configuration problems will be reported as a bright red message at the bottom of the Analog Monitor. Signal traces are displayed for diagnostic purposes and to insure that the trigger signal is being received. (Click the labels will cycle through the channels.) The trigger threshold should be set just above the base voltage and it is display as a red line. Every time the trigger signal crosses this line, a ping is logged. At this point, if the wiring and Analog Monitor configuration is correct, one should be able to start SURVEY, see data coming in on the correct signal traces and view the Ping Number field on the Analog Monitor steadily increasing. The scrolling data window in SURVEY will also display the sub-bottom profiling data.
Notes: 11

## Slide 12
Analog Settings – Triggers & Sweep Rates
External Trigger: The sub-bottom system is being triggered by another source and HYPACK just ‘listens’ for the returns.
Internal Trigger: HYPACK provides a trigger to the sub-bottom system via the NI USB A/D box. The user can control the Trigger Interval from the Analog Settings box.
Internal – SB Divisible: Used to avoid interference between two sub-bottom systems.
Sample Period: How long the Sub-Bottom driver listens for returns.
Sample Delay: How long the sub-bottom driver waits after the ping before starting listening. This feature can be used in deeper water to reduce the length of the water column in the data.
Notes: 12

## Slide 13
Analog Settings – Triggers & Sweep Rates Continued
In the example, SBP System 1 is triggered every 250 ms with sweep length of 70 ms (±53 m). The SBP System 1 trigger is divided by 2 to give SBP System a trigger interval of 500 ms with a 85 ms trigger delay and a 150 ms sweep length.
One can tell if there will be any acoustic interference between the systems if the “blue” sweep lines occupy the same time slice; as one can see this is not the case and the result will be two interference-free datasets.
As an example, the general rules of thumb for configuring the triggers and sweep length for various sub-bottom profilers, in a maximum water depth of 30 meters, are tabulated below. Note, that to convert from meters to milliseconds one must divide by 0.75.
Note: it is a good idea to set the sweep value to a bit more than one calculated to allow a safety margin for unknown seabed conditions.
Notes: 13

## Slide 14
Running SURVEY (Single SBP)
In SURVEY the sub-bottom profiling data is viewed in the Scrolling Data Window.
Notes: 14

## Slide 15
Running SURVEY (Dual SBP)
If one is simultaneously acquiring two channels of sub-bottom data there will be two instances of the Scrolling Data window showing Channel 1 & 2 respectively.
Notes: 15

## Slide 16
Sub-Bottom Controls
There are two Sub-Bottom Controls (Options & Sub-Bottom Corrections) located at the top of the Scrolling Data window:
Options
This window allows the Scrolling Data window to be vertically sized using Autoscale or Manual values. Options to display a grid on the sub-bottom data imagery are available and the grid can be displayed in milliseconds or meters.
Sub-Bottom Controls in SURVEY
Scrolling Data window display options
Note: these corrections are not applied to the SEG-Y data files as HYPACK always records the raw data to the SEG-Y file.
Notes: 16

## Slide 17
Sub-Bottom Controls
There are two Sub-Bottom Controls (Options & Sub-Bottom Corrections) located at the top of the Scrolling Data window:
Sub-Bottom Corrections: This window controls the data Band Pass Filtering, TVG, Bottom Tracking and Signal Display Modes.
Sub-Bottom Controls in SURVEY
Note: these corrections are not applied to the SEG-Y data files as HYPACK always records the raw data to the SEG-Y file.
Band Pass Filtering reduces extraneous noise recorded by the sub-bottom receiver during acquisition. In general the recommended starting point for filtering sub-bottom data is use a low pass start frequency of half of the sub-bottom transmit frequency and a high pass end frequency of double the sub-bottom transmit frequency. For example if you are using a sub-bottom profiler transmitting at 4 kHz then use band pass filtering of between 2 kHz to 8 kHz as a starting point and adjust accordingly to achieve good quality data. Generally additional band pass filtering should not be applied to Chirp data due to the match filtering and correlation that is applied to the signal arrivals by the sub-bottom profiler manufacturer.
TVG (Time Varied Gain) has three levels (TVG1, TVG2 & TVG3) that can be applied to enhance the real-time data display. TVG1 rate applies through the water column, TVG2 rate applies from the seabed bottom tracking through the seabed strata and TVG3 rate applies during the final part of the sweep period. Set TVG3 to a lower rate than TVG2 to prevent the saturation that might otherwise occur if the gain continues to increase during long sweep periods. Set a delay period for when you require the TVG3 rate to apply. The TVG3 delay begins at the seabed bottom tracking (start of the TVG2 ramp). Note: If you set a TVG3 delay period of zero, the TVG2 rate will apply from the seabed tracking to the end of the sweep. For shallow penetration sub-bottom profiling systems only TVG1 & TVG2 are generally used. The optimal combination varies, depending on the sub-bottom system and the depth of penetration.
Notes: 17

## Slide 18
Sub-Bottom Controls
There are two Sub-Bottom Controls (Options & Sub-Bottom Corrections) located at the top of the Scrolling Data window:
Sub-Bottom Corrections: This window controls the data Band Pass Filtering, TVG, Bottom Tracking and Signal Display Modes.
Sub-Bottom Controls in SURVEY Continued
Note: these corrections are not applied to the SEG-Y data files as HYPACK always records the raw data to the SEG-Y file.
Bottom tracking can be determined by one of three methods:
Calculate: Calculation based on the signal amplitude levels
using the user defined blanking, gate size and sensitivity values.
Manual: Manually setting the depth for the bottom tracking.
Sensor: Reading the bottom tracking from the sub-bottom system.
Note: the bottom tracking location can be set by clicking where the red horizontal bottom track line should appear in the Signal Amplitude window in the Scrolling Data window.
TVG (Time Varied Gain) Signal Display Modes (Color by Amplitude) are available to adjust how the data is visualized. The display scale can be set to Autoscale or manually adjusted:
    Unipolar – gray scale image in which the negative signal amplitude is zeroed. This works well with Pinger and Chirp data.
    Bipolar – gray scale image in which both positive and negative signals are displayed with the zero signal level colored 50% gray. This works well for Boomer/Sparker data.
    Rectified – gray scale image displayed as the absolute signal amplitude value where negative signals are converted to positive values. This works well for Boomer/Sparker data.
    Color – color version of the Bipolar display.
Notes: 18

## Slide 19
Dual SBP Analog Collection in SURVEY
Notes: 19

## Slide 20: Setting up a NI-DAQ Device: Analog SBP & SSS

## Slide 21: NI-DAQ Models
NI USB-6221 BNC – current HYPACK recommendation (Legacy Product
Research summary spreadsheet of replacement models.
New 16-bit recommendations are:
      USB-6341 with BNC 2110
      USB-6212 BNC
Chesapeake Technologies
      USB-6210 (no triggering support) – works with HYPACK
      USB-4431 (24-bit) – does not work with HYPACK

## Slide 22: Installing NI-DAQ Software
Install the NIDAQ951f2.exe onto the acquisition PC & perform software updates. This can take an hour or more!
Connect NI-USB device & start NI-DAQ software.
Test system.
Default RSE floating signal
source (Reference Signal Ended).
The NI-DAQ software should not be running when using HYPACK.

## Slide 23: Disable Unnecessary NI-DAQ Services
The NI driver installs many services, most of which are started automatically.
Only four are required for actually using the device.
Go to Control Panel->Administrative Tools->Services and disable the unneeded services to avoid potential port conflicts with other devices. Enable/disable the NI services as shown below:

## Slide 24
General Analog Monitor Information
The Analog Monitor is used to configure the analog settings for generating triggers and for listening for returns.
Each analog Sub-Bottom system will have its own particular settings to maximize the quality of the returns.
When SURVEY is started, the drivers will automatically start Analog Monitor.
Select the “I/O Channels” button and for each field one needs to configure the channel on the NI USB device that the signal is wired to. Each of the Channels can be assigned a custom label or name applicable to the SBP system in use, i.e. “Sparker Signal”.
The default trigger voltage levels of -5V/+5V should generally be used but the voltage levels for Channel 1 and/or 2 need to be set at this time. The recommended signal voltage levels for Pinger/Chirp SBP systems are between -5V/+5V and -2V/+5V depending on the age of the system whereas hydrophone arrays for boomers/sparkers/etc generally output voltages in the -1V/+1V to -5V/+5V volt range depending on the sensitivity of array, the gain on the hydrophone preamp and the reflectivity of the seabed.
Use the default Terminal Mode (RSE) and default channel sample rate except for advanced users.
Notes: 24

## Slide 25
Analog Monitor Information Continued
The voltage values set for Channel 1 & 2 can be considered as a “base gain” for the channel and it is important not to clip the incoming signals as these clipped data cannot be recovered. A Rule of Thumb is to set the voltage range about one third higher than the actual input signal voltage.
Any configuration problems will be reported as a bright red message at the bottom of the Analog Monitor. Signal traces are displayed for diagnostic purposes and to insure that the trigger signal is being received. (Click the labels will cycle through the channels.) The trigger threshold should be set just above the base voltage and it is display as a red line. Every time the trigger signal crosses this line, a ping is logged. At this point, if the wiring and Analog Monitor configuration is correct, one should be able to start SURVEY, see data coming in on the correct signal traces and view the Ping Number field on the Analog Monitor steadily increasing. The scrolling data window in SURVEY will also display the sub-bottom profiling data.
Notes: 25

## Slide 26
Analog Settings – Triggers & Sweep Rates
External Trigger: The sub-bottom system is being triggered by another source and HYPACK just ‘listens’ for the returns.
Internal Trigger: HYPACK provides a trigger to the sub-bottom system via the NI USB A/D box. The user can control the Trigger Interval from the Analog Settings box.
Internal – SB Divisible: Used to avoid interference between two sub-bottom systems.
Sample Period: How long the Sub-Bottom driver listens for returns.
Sample Delay: How long the sub-bottom driver waits after the ping before starting listening. This feature can be used in deeper water to reduce the length of the water column in the data.
Notes: 26

## Slide 27
Analog Settings – Triggers & Sweep Rates Continued
In the example, SBP System 1 is triggered every 250 ms with sweep length of 70 ms (±53 m). The SBP System 1 trigger is divided by 2 to give SBP System a trigger interval of 500 ms with a 85 ms trigger delay and a 150 ms sweep length.
One can tell if there will be any acoustic interference between the systems if the “blue” sweep lines occupy the same time slice; as one can see this is not the case and the result will be two interference-free datasets.
As an example, the general rules of thumb for configuring the triggers and sweep length for various sub-bottom profilers, in a maximum water depth of 30 meters, are tabulated below. Note, that to convert from meters to milliseconds one must divide by 0.75.
Note: it is a good idea to set the sweep value to a bit more than one calculated to allow a safety margin for unknown seabed conditions.
Notes: 27

## Slide 28: Wiring the NI-USB DAQ
There are many possible analog triggering & signal configurations:
    Single channel SBP with internal or external trigger.
    Two channel SBP with internal triggers (divided).
    Two channel SSS with internal or external trigger.
    Two channel SSS & two channel SBP with internal trigger.
Configuring the NI-USB 6221, 6341 & 6212:
Sounding Better January 2018

## Slide 29: Configuring Single Channel SBP – Internal Trigger
In this configuration the Analog Output 0 is sent to Analog Input 0.
On Analog Input 0 there must be a BNC T so that the trigger can be sent to the SBP.
Analog Input 1 is connected to the SBP signal
output. Set the signal source to Floating Source (FS) *
SBP Ch 1 Signal Output
48 Hz passive HPF
SBP Trigger Input
*
*
Analog
Monitor
BNC T
Passive High-Pass Filter
(resistor & capacitor)
Set voltage to ±1/3 higher
than input voltage
Uncheck this box

## Slide 30: Configuring Single Channels SBP – Internal Trigger
Trigger
Configuration
In this example a Pinger (Ch 1) is being used for the survey.
Set the Trigger Mode to Internal.
Set the Pinger trigger to 250 ms & the sweep rate to 70 ms (52 m).

## Slide 31: Configuring Single Channel SBP – External Trigger
In this configuration the Trigger from the SBP or external trigger box is sent to Analog Input 0.
Analog Input 1 is connected to the SBP signal
output. Set the signal source to Floating Source (FS) *
SBP Ch 1 Signal Output
48 Hz passive HPF
SBP Trigger Input
*
*
Analog
Monitor
Uncheck this box

## Slide 32: Configuring Single Channels SBP – External Trigger
Trigger
Configuration
In this example a Pinger (Ch 1) is being used for the survey.
Set the Trigger Mode to External.
Set the Pinger sweep rate to 70 ms (52 m).

## Slide 33: Configuring Two Channels SBP – Internal Trigger
SBP Ch 1 Signal Output
SBP 1 Trigger Input
*
*
BNC T
Analog
Monitor
SBP 2 Trigger Input
BNC T
SBP Ch 2 Signal Output
In this configuration the Analog Output 0 is sent to Analog Input 0.
Analog Output 1 is sent to Analog Input 1.
On Analog Input 0 & 1 there must be a BNC T so that the
triggers can be sent to the two SBP. Systems.
Analog Input 2 is connected to the SBP signal output Ch 1 & Analog Input 3 to Ch 2.
48 Hz passive HPF

## Slide 34: Configuring Two Channels SBP – Internal Trigger
Trigger
Configuration
In this example a Pinger (Ch 1) & Sparker (Ch 2) are being used for the survey.
Set the Pinger trigger to 250 ms & the sweep rate to 70 ms (52 m).
Divide the Trigger 1 (250 ms) by two to make Trigger 2 500 ms.
Delay Trigger 2 by 80 ms so these is no interference with the Pinger (Ch1).
Set the Sparker (Ch 2) sweep rate to 150 ms (112 m) for no interference with the Pinger (Ch1).

## Slide 35: Configuring the Analog Monitor, Setting Triggers, Delays & Sweep Length
Setting the Trigger Intervals & Sweep Rate
As an example, the general rules of thumb for configuring the triggers and sweep length for various sub-bottom profilers, in a maximum water depth of 30 meters, are tabulated below. Note, that to convert from meters to milliseconds one must divide by 0.75:
Sounding Better April 2017

## Slide 36: Configuring Two Channels SBP & SSS– Internal Trigger
SBP Ch 1 Signal Output
SBP 1 Trigger Input
*
*
BNC T
Analog
Monitor
SBP 2 Trigger Input
BNC T
SBP Ch 2 Signal Output
SSS Trigger Input
SSS Port Channel
SSS STD Channel
BNC T
BNC T
48 Hz passive HPF

## Slide 37: Configuring Two Channels SBP & SSS– Internal Trigger
Trigger
Configuration
In this example a SSS, Pinger (Ch 1) & Sparker (Ch 2) are being used for the survey.
Set the SSS & Pinger trigger to 100 ms & the sweep rate to 100 ms (75 m).
Divide the Trigger 1 (100 ms) by five to make Trigger 2 500 ms.
Trigger delay will not help with interference between the systems.
Set the Sparker (Ch 2) sweep rate to 150 ms (112 m).

## Slide 38: Configuring the NI USB-6210 (Chesapeake Technologies)
SBP Ch 1 Signal Output
SBP 1 Trigger Input
Analog
Monitor
48 Hz passive HPF
NI Software
used for Trigger
In the NI Test Panel Counter I/O:
Set mode to Pulse Train Generator
Set Frequency to 4 for 250 ms trigger
(or any desirable trigger interval)
Set Duty Cycle to 3
A trigger of 250 ms will know be
generated for the SBP or SSS.
A SSS will require CH2 input for the
Other SSS channel.
The NI USB-6210 can be use with HYPACK but the trigger must be generated in the NI software or other external source. The NI USB-6210 can be used for SBP or SSS data collection.

## Slide 39: Making a 48 Hz Passive High-Pass Filter Box
A 48 Hz PHP filter can remove the characteristic hydrostatic “swell” (wiggle) associated with towed hydrophone array. This PHP filter is not necessary for transducer based systems. Refer to the images below to build a 48 Hz passive high-pass filter box.
SBP Ch 1 Signal Output
NI-DAQ
1W6 Capacitor
Resistor
(brown/black/orange)

## Slide 40: Sub-Bottom Data Processing
Low signal level data

## Slide 41
Introduction
Located under ‘Processing’ menu
Used to process small & large SEG-Y or JSF datasets.
Full suite of processing features.
Digitizing layers & color polygons
Mark targets
3D fence diagrams
Manually digitize acoustic layers
Mark targets
Notes: 41

## Slide 42
Loading Files
Select “New Session” to load SEG-Y/JSF/Log files into a new project. HYPACK can read most compliant third party SEG-Y files.
To continue working on an existing project select “Open Session” and click on the SBP.xml file to load the data files & user settings.
If the user clicks “New Session” and there are existing files in the SBP folder, now HYPACK makes a backup of them rather than deleting the original files in the SBP folder.
Navigation can be read from the SEG-Y (or JSF) file, RAW file or EDT file. In HYPACK MAX (SBMAX) one can edit the navigation in a RAW file for “spikes” and apply the corrected EDT navigation to the sub-bottom profiling data.
Notes: 42

## Slide 43
Data Processing
Low signal level data
Raw Boomer data
Processed Boomer data
  Auto Range, TVG & Bottom Tracking button under the Display Tab in the Settings menu which can provide initial settings for the data display
  The Settings window is used to correct the dynamic range of the data, apply band pass frequency filtering, time varied gain (TVG), bottom tracking, water column blanking (removing water column noise) and swell filtering to the data.
  The Dynamic Range tab controls have options to view the data in Bipolar, Rectified or Unipolar modes and apply different color palettes to visually enhance the data.
  TVG curves (exponential & user defined) can be applied to the data as well as user defined TVG curves. These curves can be saved for each line or project and re-imported/applied at any later stage.
Notes: 43

## Slide 44
Digitizing Layers
Digitize up to 20
different layers (custom names & colors)
Apply different sound velocity for water and sediment
Layers can be exported to EDT or XYZ format
Annotation Tool
Manually digitize acoustic layers
  Select the Reflector number and manually digitize each geological layer.
  To digitize “left mouse click” (+) to add a point. Shift click (-) to remove a point & Ctrl click (-) to move a point.
  Select “Annotation tool” under the Display Tab to add depth & sediment thickness information at the curser location. Annotations can be added to the data or removed in the same way as Reflector editing.
Notes: 44

## Slide 45
Map View of Digitizing Layers
Isopach/depth digitizing “points”
  Reflector (layer) digitizing depths or isopachs (sediment thickness) can be seen plotted on the View Tracks window as digitizing is progressing.
  This is a useful quality control tool as the consistency of the interpretation can be gauged by reviewing the interpretation on adjacent or cross-lines.
  Points for each of the 20 Reflectors can be viewed in by absolute depth or isopach (sediment thickness).
View Tracks window showing the digitized reflector isopach interpretation values represented as colored isopach (thickness) points for three survey lines. An editable color scale bar is provided in the View Tracks tab of the Display.
Notes: 45

## Slide 46
Coloring Layers
Color up to three separate polygons
  Another useful feature is the ability to be able to color each geological unit as an isopach polygon using a custom color palette and transparency.
Colored geological polygon
Notes: 46

## Slide 47
Targeting
Targets
Add, edit, or delete targets in Target Editing Mode.
Drag target's handle to mark depth & isopach.
Saved to SBP.tgt in the project folder.
Targets also displayed in View Tracks.
Notes: 47

## Slide 48: Sample Session – Data Processing

## Slide 49
Exporting Data & Corrections
Data interpretations generated from digitizing the various reflective sub-surfaces can be output as ASCII XYZ or HYPACK EDT files. Various corrections can be applied to the data outputs such as:
Sound velocity correction in the water column (average value or apply a sound velocity profile) and separate velocity corrections for saturated sediment or rock.
Tide corrections using a HYPACK tide file.
Layback corrections to the data outputs if these were not specified in HYPACK hardware. If the data were acquired in HYPACK and HARDWARE was correctly figured then the coordinates in the SEG-Y file will be corrected for the SBP sensor position.
Latency corrections between measurement and transmission to the data acquisition computer. See Sounding Better May 2018 for details.
Interpretation outputs can be trimmed to a border file.
A separate reference file is generated with each ASCII XYZ file high-lighting the corrections applied to the data.
Screen shots can be captured in various image formats (PNG, JPG or BMP), with or without the superimposed reflector interpretation. A coordinate reference file is produced with each image which allows the image to be used as a vertical seismic curtain in third party software packages.
Exported data can be used in the TIN MODEL to generate surfaces and volumes or in other third party GIS/CAD software packages.
Notes: 49

## Slide 50: Sample Session – Exporting Data
Notes: 50

## Slide 51
3D Fence Diagrams
HYPACK SUB-BOTTOM has the ability to produce 3D fence diagrams of the sub-bottom profiling lines with superimposed reflector interpretation and colored isopach polygons.
The fence diagram can be rotated in any direction and the transparency of the data controlled. The fence data can also be trimmed to a border file to highlight a particular area of interest.
This is a useful tool for visualizing the data in three dimensions to provide a better understanding of the sub-surface geology..
Use Shift left mouse click to rotate the Fence.
Mouse wheel to zoom in/out.
Right mouse click to pan.
Notes: 51

## Slide 52: 3D Fence Diagrams
3D fence diagram of three parallel sub-bottom profiling lines showing superimposed interpretation and scale bars.

## Slide 53: 3D Fence Display
3D fence diagram of two intersecting sub-bottom profiling lines.

## Slide 54: Sample Session – 3D Fences
Notes: 54

## Slide 55: Thank You !
January 2020
HYPACK on Youtube.com ( Historical Sessions ) HYPACK Live Chat
HYPACK on Youtube.com ( Newer Sessions ) HYPACK Ustream
HYPACK SUPPORT Site HYPACK Website
Links to more information:
Contact Us:
Sales@HYPACK.com
Help@HYPACK.com
(860) 635 - 1500