## Slide 1: Ancillary Uses of HYPACK
HYPACK 2020 Training Event
January 2020

## Slide 2: HYPACK SURVEY: GHOST SHAPES
Enter the final position for a rig or barge move and draw a ghost shape (orange).

## Slide 3: Sending SURVEY Windows Across the Network to Non-HYPACK Computers.
HYPACK Computer
Non-HYPACK Computer
Running SURVEY VIEWER
Non-HYPACK Computer
Running SURVEY VIEWER
Non-HYPACK Computer
Running SURVEY VIEWER
Non-HYPACK Computer
Running SURVEY VIEWER
LAN or Wireless Network
Windows 10 and Windows 7 limit the number of broadcast clients to 8.
SURVEY VIEWER

## Slide 4: Password Protected Sharing = Off
For SURVEY VIEWER to function properly on Windows 7 computers, you will need to go into the Advanced Sharing Settings and ‘Turn off password protected sharing’ on the computer running HYPACK SURVEY..

## Slide 5: Remote Viewer over Web

## Slide 6: Remote Viewer Control
Control Survey remotely from PC without HYPACK Key
Basic commands sent. Logging, Targeting etc.

## Slide 7: WebIF.DLL: Another Option…
View the SURVEY program (Area Map and Data) from an Intranet connection.
Check out the WEBIF presentation on this DVD under the ‘Survey’ group.

## Slide 8: 3D Vessel Monitoring
In the image there is a crew boat approaching the barge with a supply boat in the background. A survey vessel is running lines in the foreground with a magnetometer. Each vessel is controlled from a separate computer on our internal wireless network and collected on the main observation computer. The 3DTV program was used in its new multiple vehicle tracking capacity. The depth of the magnetometer was controlled by changing the draft of that mobile.
Barge in a work site that going to be serviced by multiple vessels including a supply boat and a crew boat.
The requirement is that all vessels are able to share the position, heading and tide corrected depth with each other.

## Slide 9: Dredge Quality Management

## Slide 10: DQM Data
DQM data is compiled for all monitored fields and saved to a database file for environmental reporting.
This includes position of the tool to remove contaminated sediment and is not limited to position, depth, bottom type of amount of material to be processed.
Each shift can be monitored and data compiled for every second of work time
Bottom characteristics can be logged and reports generated.

## Slide 11: Data to USACE DQM onboard PC

## Slide 12: Mission Planning and Line Steerage

## Slide 13: Robot remote data collection and controls

## Slide 14: UAV and USV Data Collection

## Slide 15: UAV and USV Data Collection
Real time data collection
  Onboard
  Remotely logged
Can send waypoints to remote vessel

## Slide 16: HYPACK UAV data in 4 dimensions
Lidar
Multibeam Bathy
ADCP
Water Quality
Sidescan Imagery
Tidal Measurement

## Slide 17: Live Turbidity Monitoring

## Slide 18: YSI_Turbidity.dll with YSI EXO

## Slide 19: Auto Import Tides from NOAA
Manual Tides program
If NOAA tide station is known it will auto populate
Can save out as *.tdx and *.tid file
Can import into TideDr.dll device driver in HYPACK Hardware

## Slide 20: NOAA Online Tide Reader
NOAATides.dll
Driver will read tide level from NOAA server and apply to the SURVEY or DREDGEPACK
Datums can be selected to match project specification
Data is logged to *.Raw data files for processing

## Slide 21: CUSTOM Shape Displays in SURVEY
Images can be saved as BMP and displayed in SURVEY Map Windows
Scalable Shape
Easily identifiable vessel tracking

## Slide 22: RIG MOVES

## Slide 23: Step 1: Boat Shape Editor
Create your boat shape.
The Boat Origin Reference Point is at the X=0, Y=0 point.
Set 1 or 2 anchor points.
  One Anchor Point: SURVEY will determine the final rig position using the Anchor Point and the heading.
  Two Anchor Points: SURVEY will determine the final rig position using the two Anchor Points.

## Slide 24: Step 1: Boat Shape Editor
Anchor #1
Anchor #2

## Slide 25: Step 2: HYPACK HARDWARE
The actual position of the Rig is the ‘Boat’ mobile.
  In this case, we are positioning the rig with an RTK GPS with directional antenna, using the GPS.DLL.
The final target position of the Rig is the ‘Rig Site’ mobile.
  We will use the BARGE.DLL to set the final target position for the rig.

## Slide 26: BARGE.DLL
In the ‘SETUP’ for the BARGE.DLL:
  To position the rig using one Anchor Point and a heading, click just the ‘Anchor 1’ box and enter final position and heading (below).
  To position the rig using two Anchor Points, click both the Anchor 1 and Anchor 2 boxes and enter the final positions.

## Slide 27: Step 3: SURVEY
The final position of the rig will be drawn in Blue.
  This is determined based on the information in the BARGE.DLL.
The current position of the rig is currently shown in Red.
  We have set the Fill Color for the main ‘Boat’ mobile to red. Your color may be different.
  We have also set the transparency for the boat shape so that we can see the final target position (blue) beneath the current position (red). (Done in the Vessels menu.)

## Slide 28: Vessel Settings: Current Position
Select Primary Vessel:
Make Opaque
Set Color:
Step 3: SURVEY

## Slide 29: Vessel Settings: Final Position
Select Rig Vessel:
Set Transparency
Set Color:
Step 3: SURVEY

## Slide 30: SURVEY: Barge Info Window
Displays the distance and bearing each Anchor Point needs to move.
Displays the current heading and the required heading.

## Slide 31: Voila!

## Slide 32: BARGE MANAGEMENT

## Slide 33: Barge Management in HYPACK
The main Barge wants to see Tug1, Tug2, Tug3 and Tug4.
Tug1 wants to see the Barge, Tug2, Tug3 and Tug4.
Etc., etc., etc.

## Slide 34: Hardware Requirements:
Main Barge:
  GPS with Directional Antenna.
  Wireless router with Omni-Directional antenna
  Computer with HYPACK SURVEY capability.
Tugs
  GPS with Directional Antenna.
  Notebook Computer with HYPACK SURVEY and Wifi capability.
Vessel IP Address Subnet
Main Barge (Boat): 192.168.5.101 255.255.255.0
Tug 1: 192.168.5.102 255.255.255.0
Tug 2: 192.168.5.103 255.255.255.0
Tug 3: 192.168.5.104 255.255.255.0
Tug4: 192.168.5.105 255.255.255.0
Network Setup:
  Each computer needs a Static IP address on a common sub-net.
  See the example below for sample settings.

## Slide 35: Setting a Static IP Address
Open the Network and Sharing Center and click on your Wireless Network Connection. The window on the left will appear.
Click the ‘Properties’ button. The window in the center will appear.
Click on ‘Internet Protocol Version 4 (TCP/Pv4) and then ‘Properties’. The window on the right will appear.
Enter the appropriate IP address and subnet address for the computer.

## Slide 36: HYPACK HARDWARE
Create a separate mobile for each vessel. The vessel set-up on the Barge is shown to the right.
On each vessel:
    Use the GPS.DLL to determine your position and heading.
    Use the NMEAOUTPUT.DLL to output your position and heading to the other vessels.
To see the other vessels:
    Use the GPS.DLL to read their position and heading.
Vessel Setup on Barge
Vessel Setup on Tug 1

## Slide 37: Configuring the NMEAOUTPUT.DLL
On each vessel, we will configure the NMEAOUTPUT.DLL to broadcast its position and heading data using a UDP connection.
Each vessel will use a separate Read/Write Port value.
NMEAOUTPUT.DLL Type Client/Server Read/Write Port
Barge (Boat) UDP Server 9101
Tug2 UDP Server 9102
Tug3 UDP Server 9103
Tug4 UDP Server 9104
Tug5 UDP Server 9105

## Slide 38: Configure the NMEAOUTPUT.DLL
Settings Window: Output GGA & HDT.

## Slide 39: Configure the NMEAOUTPUT.DLL
Set the update rate at 1Hz.

## Slide 40: Reading the Broadcast from Each Vessel
On the Barge, we will use the GPS.DLL to read the position data from Tug 1
We are just reading the Position and Heading data from each vessel’s broadcast.
We’ll specify a Network connect, using UDP protocol and acting as a Server. Set the Read Port and Write port to the proper value for the vessel.

## Slide 41: HYPACK SURVEY

## Slide 42: Thank You !
January 2020
HYPACK on Youtube.com ( Historical Sessions ) HYPACK Live Chat
HYPACK on Youtube.com ( Newer Sessions ) HYPACK Ustream
HYPACK SUPPORT Site HYPACK Website
Links to more information:
Contact Us:
Sales@HYPACK.com
Help@HYPACK.com
(860) 635 - 1500