## Slide 1: Hypack Unmanned
HYPACK 2020 Training Event
January 2020

## Slide 2: What are Unmanned Systems?
Underwater (AUVs)
Autonomous Underwater Vehicles
Vehicle tracking/Processing
On the Surface (USVs)
Unmanned Surface Vessels
Bathymetric Mapping
In the Air (UAVs)
Unmanned Aerial Vehicles
Topographic Mapping

## Slide 3: How is HYPACK Involved?
Sensor integration through Hypack drivers
Mission planning through Hypack combined with GNSS systems and autopilot system enables autonomous data collection
Data from sensors that are supported by Hypack can be visualized in real time along with system health
Data acquisition and processing can be done in Hypack

## Slide 4: UUV platforms
UUV(data processing): Hydroid (Kongsberg)
Iver3 OceanServer
YSI has partnered with OceanServer to produce i3XO, combining Iver3 with their water quality sonde and ADCP
Kongsberg also has Gavia solution- similar to a deep water REMUS

## Slide 5: USV platforms
Seafloor Systems EchoBoat
Teledyne Z Boat
HyCat

## Slide 6: Survey planning for autonomous vehicles

## Slide 7: Mission Planning
Plan autonomous mission in Hypack shell using
Line Editor/Border Editor, autopilot, or a proprietary navigation system

## Slide 8: Mission Planning
Upload mission directly or export mission plan in 3rd party/proprietary format.
Can import GPX and Mavlink formats in Mission Planning, can export GPX, MAVlink, MOOS-IvP BHV, Teledyne ZRP
Line report gives you a time estimate based on line distance and input survey speed

## Slide 9: Mission Planning- FAA Charts
To fly a drone “commercially” you need an FAA part 107 license
Part 107 teaches you how to read VFR charts (navigate through regulated airspaces), laws surrounding airspace, basic weather observation skills, flight reporting and requirements, etc.
Flying a drone
for non recreational purposes is commercial use
VFRs are available to download from the FAA as free products, similar to marine charts

## Slide 10: Survey acquisition for autonomous vehicles

## Slide 11: Mission Planning
Autopilot works with mission plans to steer, navigate, and collect data autonomously- does not require user input!
The drivers use standard NMEA- marine GPS commands to communicate between GPS, autonomous vehicle, and autopilot
Report position, attitude, basic system health
Autopilot interfaces
Example of system position

## Slide 12: Adaptive Line Planning
AutoLines.dll
1. Survey tracks MBES coverage during logging
2. When logging ends, a new planned line is generated.
3. When logging begins, a new tracking line begins on the opposite side of the vessel.

## Slide 13: Remote Viewing Platform
Observe & interact with autonomous operations using HYPACK remote tools
  View vessel position
  Manually control logging
Use any web enabled device
  smartphones, tablets, computers
Controlled access and secured views

## Slide 14: Real time LiDAR
Real-time 3D data visualization, including high-density point clouds from LiDAR sensors mounted on autonomous aerial platforms.

## Slide 15: Collecting water quality data
Can collect water quality data from a YSI EXO or 6660 Sonde with ysi6660.dll or ysiexo.dll in Hypack
Good applications for studies with USV or potential UAVs

## Slide 16: Data processing for autonomous vehicles

## Slide 17: Data Converter
Data Converter can convert SSS and MBES for data processing. LiDAR data for UAVs can be logged in Hypack proprietary format (HSX).
Ideal tool for autonomous platforms with proprietary logging features.
EDGETECH
JSTAR
KLEIN SDF
ODOM TDY
CMAX
MARINE SONIC
IMAGENEX
ELAC HYDROSTAR
KONGSBERG
Generic Sensor Format
APPLIED SIGNAL
SwathPlus
Kraken TIL
XTF files created by other logging systems
DATA CONVERTER
MST
XSE
83P
SDF
HYPACK file
XTF
CM2
JSF
ALL
GSF
81S
IMG
s7k
SXI/ SXP
TDY
D1P
TIL

## Slide 18: Data Splitter and Joiner
Post-process data collected autonomously.
Remove turns
Create traditional-looking survey track lines from a contiguously logged AUV file
Launch the tool directly from the Data Converter or Utilities-> File work -> Data Splitter/Joiner

## Slide 19: MBMAX Tools
Can process multibeam, single beam, side scan data.
Can merge XYZ files with .all files to join sonar and LiDAR data
MBMax64 can embed images with position for data correlation

## Slide 20: Auto-Processing
-Auto-processing for Multibeam data
NOTE: Cannot process files with MBES and LiDAR
-Enable option through survey in shell
-Set up Read Parameters in MBMAX
-As soon as the user stops logging, parameters are applied and an hs2x file is ready for quick load
Great for autonomous applications!

## Slide 21: MBMax Tools
Can also apply pressure data to bathy data from an underwater vehicle w/smoothing for depth correction

## Slide 22: Vegetation Filter
Window Size: The along profile segment distance
Overlap Percent: Overlap between window segments
Gate Size: Elevation above and below interpolated ground level, filters data outside of gates

## Slide 23: Vegetation Filter
Filtering allows for analysis of ground elevations

## Slide 24: RGB Point Clouds
You import geotiffs into Hypack Real Time Cloud to color your XYZ file with RGB colors- producing a realistic looking point cloud!

## Slide 25: Processing water quality data
Process water quality data in SBES Editor
Open Read Parameters, choose specialty device, can read two data types at a time and view it as a time series
Can view profiles, edit data, view and edit spreadsheet, filter, etc.

## Slide 26: Water Quality data continued….
Salinity in Mystic Harbor
Can save data as an EDT or XYZ, modeled and displayed using TIN model

## Slide 27: Water Quality continued…
Data collected by HyCat at Sontek SRC Facility

## Slide 28: Water quality continued
Data from HYCAT with bathymetry, contours, temperature, SSS mosaic

## Slide 29: HYPACK LiDAR Payload
November 2019
PORTABLE LIDAR SOLUTION FOR TOPOGRAPHIC, AERIAL, AND MARINE SURVEYING

## Slide 30: Why The HYPACK LiDAR Payload?
LiDAR is a quick and accurate way to capture difficult to obtain data
LiDAR is good for thin edge features
LiDAR can penetrate through forest canopies and dense vegetation
Quick integration with other data sources and workflows
Quick data turn around
Low cost alternative to traditional methods
Overall: Increasing efficiency and reducing risk

## Slide 31: Conducting a LiDAR Survey in HYPACK MAX/HYSWEEP

## Slide 32: Mission Planning
Plan autonomous mission in HYPACK shell using
Line Editor/Border Editor, autopilot, or a proprietary navigation system

## Slide 33: HYPACK® Survey / HYSWEEP®
User adds Velodyne and SBG to hardware, launches survey.
The SURVEY program displays the map and SBG data in real time.
The use of a matrix allows the user to see the coverage of the system in real time.

## Slide 34: HYPACK® Survey / HYSWEEP®
HYSWEEP® has an option for a topographic laser display,
where you can monitor elevation readings in real time

## Slide 35: Real Time Cloud
Real Time Cloud allows the user to see real time, geo referenced, motion corrected data as it is recorded. User can set display colors to show intensity from LiDAR unit or depth/elevation colors.

## Slide 36: Remote Viewing Platform
Observe & Interact with autonomous operations using HYPACK remote tools
  View vessel position
  Manually control logging
Use any web enabled device
  smartphones, tablets, computers
Controlled access and secured views

## Slide 37: Processing LiDAR Data

## Slide 38: Data Splitter/Joiner
Post-process data collected autonomously.
Remove turns
Create traditional-looking survey track lines from a contiguously logged AUV file
Launch the tool directly from the Data Converter or Utilities-> File work -> Data Splitter/Joiner

## Slide 39: MBMAX64
Main processing engine, can apply filters, edit fliers, perform sensor calibration

## Slide 40: LiDAR Editing in MBMAX64
Set Patch Test Values in Read Parameters
Edit data points in profile view or in real time cloud
Smooth GPS data
Apply SBETs to your data
Set Depth or Elevation Mode

## Slide 41: GPS filtering
The LiDAR data is generally clean of the spikes experienced in a Multi Beam Sonar survey.
The data can be cleaned with a series of filters. The SBG code for Narrow Lane RTK, the mode required for good data, is 7.

## Slide 42: GPS Filtering
When filtering GPS data based upon the Mode value, it is important to check the setting to delete soundings between deleted position points so that bad GNSS does not affect the quality of the final product.
Unlike sonar data, LiDAR positions cannot be interpolated.

## Slide 43: Flight Sensor Data
The Tide window allows the user to check the flight data for proper elevation.
The Pitch and Roll window allows the user to view and edit the data from the IMU if necessary.
The Speed window allows the user the ability to QC the flight speed.

## Slide 44: Vegetation Filter
Accessed in MBMax64 -> Profile Window.
Interpolates ground level from min elevation
Window Size: The along profile segment distance
Overlap Percent: Overlap between window segments
Gate Size: Elevation above and below interpolated ground level, filters data outside of gates

## Slide 45: Vegetation Filter
Filtering allows for analysis of ground elevations

## Slide 46: TIN Stockpile Volumes
Quickly compute volumes of an area using a border file.
Multiple stockpiles can be measured at one time using individual borders

## Slide 47: Stock Pile Volumes
To begin the stockpile volume, a border file is required for each pile to be computed

## Slide 48: Stock Pile Volumes
Each pile is computed separately
Volume, Void, Perimeter and Area are computed for each border

## Slide 49: Final Products for LiDAR Data

## Slide 50: RGB Point Clouds
You can import Geotiffs into Hypack Real Time Cloud to color your XYZ file with RGB colors; producing a realistic looking point cloud!

## Slide 51: Exportable Products
Portable web cloud format
Autocad DXF
Point cloud colored by RGB

## Slide 52: Payload System Specifications

## Slide 53: Payload Overview
- Computer running WINDOWS 10
HYPACK MAX® / HYSWEEP® Software license
- Velodyne VLP-16 Puck Lite LiDAR unit
SBG Ellipse-2D Dual Antenna compact inertial navigation system with integrated Dual-antenna survey-grade RTK GNSS receiver
Onboard rechargeable power supply with 3 hours run time
IP67 rated enclosure with extendable and retractable antenna arms
Pelican case for secure transport that houses spares

## Slide 54: Key Capabilities
-Fully contained LiDAR data collection tool with GNSS
Independent, stand alone solution
-Fixed antenna offsets (1m) eliminate need for repeat heading calibrations
-Can be mounted on any vehicle platform including UAV’s
-System weight is 7.5 lbs
-Can fit on any industrial drone that can lift 7.5 lbs and over
ex: DJI, Freefly, Inspired Flight, Skyfront, and Harris Aerial

## Slide 55: VLP Puck Lite
Laser: Mechanical/ Electrical/ Operational
• 16 Channels
• Measurement Range: Up to 100 m
• Accuracy: ±3 cm (Typical)
Weight 590 grams
• Single and Dual Returns (Strongest, Last)
• Power Consumption: 8 W (Typical)
• Laser Product Classification: Class 1 Eye-safe per IEC 60825-1:2007 & 2014
• Wavelength: 903 nm

## Slide 56: Velodyne Channels
Offers 16 channels that can be activated or disabled
Range filter- set min and max elevations, filter out low elevations that can introduce noise
Angle filter- set min and max angles, filter will keep data within specified angles

## Slide 57: Ellipse 2D mini GNSS/INS
0.1° Roll and Pitch over 360°
0.2° Heading (Dual Antenna GNSS)
5 cm Real-time Heave, adjusted to the wave period
2 cm RTK GNSS Position (option)
Key Features:
Very Low Noise Gyroscopes, High Quality Accelerometers
Survey-Grade L1/L2 GNSS Receiver
Differential Corrections (RTCM)
200 Hz Output Rate – Typically collected at 50 Hz
2 year warranty

## Slide 58: Example Data
Area of low vegetation, grass, soil @ 20 meters altitude
Moderate reflectivity
Average vertical uncertainty= +/- 5cm

## Slide 59: Example Data
Area of Black Asphalt @ 20 Meters altitude
Low reflectivity, high absorption
Average vertical uncertainty = 9 cm (±6 cm)

## Slide 60: Payload Mounted To A DJI Matrice 600

## Slide 61: Back Panel of HYPACK LiDAR Payload

## Slide 62: HYPACK LiDAR Payload Sample Data

## Slide 63: Sample Data Processing In MBMAX64

## Slide 64: HYPACK LiDAR Payload Sample Data

## Slide 65: HYPACK LiDAR Payload Benefits
Easy to use, turn key solution
Versatile functionality
Cost effective
Familiar interface for HYPACK users
Fixed offsets make for easy set up and initialization in the field
3 hour run time increases efficiency
Accurate LiDAR solution

## Slide 66: Potential Applications
  Shoreline/obstruction charting for navigation
  Pipeline mapping
  Infrastructure assessments
  Beach erosion surveys
  Vegetation surveys
  Bare earth analysis
  Corridor mapping

## Slide 67: HYPACK 2020 Training Event

## Slide 68: Q&A
Contact Us:
sales@hypack.com
facebook.com/hypackinc
twitter.com/hypack
linkedin.com/groups/1990404

## Slide 69
Thank You!
Webinar: HYPACK LiDAR Payload
Contact Us:
sales@hypack.com
facebook.com/hypackinc
twitter.com/hypack
linkedin.com/groups/1990404

## Slide 70: Thank You !
January 2020
HYPACK on Youtube.com ( Historical Sessions ) HYPACK Live Chat
HYPACK on Youtube.com ( Newer Sessions ) HYPACK Ustream
HYPACK SUPPORT Site HYPACK Website
Links to more information:
Contact Us:
Sales@HYPACK.com
Help@HYPACK.com
(860) 635 - 1500